## Slide 1: A Fast Large-Integer Extended GCD Algorithm and Hardware Design for Verifiable Delay Functions and Modular Inversion
Kavya Sreedhar, Mark Horowitz, Christopher Torng
Stanford University
skavya@stanford.edu
September 19, 2022

## Slide 2: Extended GCD
Computes Bézout coefficients satisfying Bézout’s Identity
Notes: Fundamental operation in number theory

## Slide 3: Extended GCD is widely used in cryptography
Computes Bézout coefficients satisfying Bézout’s Identity
Modular Multiplicative Inverse
RSA
Elliptic Curve Cryptography
ElGamal Encryption
.
.
.
Notes: Lot of work on fast XGCD algorithms in 1980s, 1990s
More recent work has focused on efficient software implementations
Two recent developments that suggest a need for faster XGCD implementations

## Slide 4: There is an increasing need for faster XGCD
Modular Inversion for Curve25519 [Ber06]
  Constant-time XGCD faster than Fermat’s Little Theorem [BY19]
Notes: BY19 is from CHES

## Slide 5: There is an increasing need for faster XGCD
Modular Inversion for Curve25519 [Ber06]
  Constant-time XGCD faster than Fermat’s Little Theorem [BY19]
Squaring binary quadratic forms over class groups [Wes19] as a VDF
  XGCD is the bottleneck
in a class group
[BBBF18]
Notes: XGCD is the primary bottleneck: 91% of execution time

## Slide 6: There is an increasing need for faster XGCD
Modular Inversion for Curve25519 [Ber06]
  Constant-time XGCD faster than Fermat’s Little Theorem [BY19]
Squaring binary quadratic forms over class groups [Wes19] as a VDF
  XGCD is the bottleneck
in a class group
255-bits, constant-time
1024-bits, not constant-time
[BBBF18]
Notes: Range of our design -> targets different application requirements

## Slide 7
Chart: 
| 2.2999999999999998 | 2.2999999999999998 | 0.20699999999999999 | 0.44700000000000001 | 4.55
Cycles | 8543 | 6253 | 8466 | 386 | 386
Clock Frequency (GHz)
255-bit constant-time XGCD
100
105
103
104
102
101
Cycle Count
[BY19]
[Por20]
[DdPM+21]
Better
No ASIC points
Software
FPGA
ASIC
Notes: Walk through these graphs: axes, constant-time performance lines, better point
No ASIC points
FPGA prototype

## Slide 8
Chart: 
| 2.2999999999999998 | 2.2999999999999998 | 0.20699999999999999 | 0.44700000000000001 | 4.55
Cycles | 8543 | 6253 | 8466 | 386 | 386
Chart: 
| 3.9940000000000003E-2 | 0.248 | 0.25 | 0.5 | 3.89 | 1
Cycles | 598 | 1143 | 1623 | 3000 | 1143 | 10650
Clock Frequency (GHz)
Clock Frequency (GHz)
1024-bit XGCD
255-bit constant-time XGCD
100
105
103
104
102
101
Cycle Count
[BY19]
[Por20]
[DdPM+21]
[ZTW21]
[AHAJS16]
[ZST+20]
Better
Better
No ASIC points
[ZST+20] is 2X faster than C++
Software
FPGA
ASIC
GNU C++ on Apple M1
Notes: State of the art is 2X faster – fundamental limit?
Not many papers in this space

## Slide 9: Current view of XGCD design space
Hardware
NCT
CT
Target Platform
Algorithm
Application Requirements
[AHAJS16]
[ZST+20]
[ZTW21]
[DdPM+21]
CT = constant-time, NCT = not constant-time
Notes: In the XGCD design space, we see that these current works focus on iterative division algorithms and provide point solutions for either constant-time or non constant-time execution

## Slide 10: We explore the broader design space
Software
NCT
CT
NCT
CT
Hardware
NCT
CT
NCT
CT
Target Platform
Algorithm
Application Requirements
[AHAJS16]
[ZST+20]
[ZTW21]
[DdPM+21]
[BY19]
[Por20]
CT = constant-time, NCT = not constant-time

## Slide 11: We explore the broader design space
Software
NCT
CT
NCT
CT
Hardware
NCT
CT
Target Platform
Algorithm
Application Requirements
[AHAJS16]
[ZST+20]
[ZTW21]
[DdPM+21]
[BY19]
[Por20]
CT = constant-time, NCT = not constant-time
Unified
Our work

## Slide 12: Hardware allows for short iteration times
Target Platform
[DdPM+21]
[BY19]
[Por20]
Our work
Number of Iterations
Constrained to ISA
From algorithm
Yes
From algorithm
No
Execution time = number of iterations iteration time
The control over iteration time in hardware opens the opportunity to accelerate simpler algorithms that require more iterations.
vs
Software
Hardware
Notes: Critical Path determines clock period, which 1 over the frequency
We observed all hardware papers built from efficient algorithms chosen in efficient software implementations. We look at if this is optimal.
Iteration time = Longest series of data-dependent operations
Since software is constrained to using instructions predefined in the processor’s instruction set architecture (ISA), software iteration times correspond to the longest set of dependent instructions. In contrast, hardware is not limited to an ISA and allows for implementing fast, wide, and custom datapaths with extremely short iteration times.
We can complete an iteration at frequencies equal to or higher than frequencies of processors
Unlike prior work

## Slide 13: GCD Algorithms Comparison
Algorithm
[DdPM+21]
[BY19]
[Por20]
Our work
GCD-preserving Transformation
a
vs
Stein [Ste67]
Euclid (300 BC)
Notes: A 2X difference is not large, why not in software?
Intuition is division is faster, software do not seem to do two-bit PM
Could be faster in software
Multiple subtractions
Two-bit in software
Is subtraction twice as fast as divison?
We extend the two-bit PM algorithm for extended GCD
We observed all hardware papers built from efficient algorithms chosen in efficient software implementations. We look at if this is optimal.
Iteration time = Longest series of data-dependent operations
Since software is constrained to using instructions predefined in the processor’s instruction set architecture (ISA), software iteration times correspond to the longest set of dependent instructions. In contrast, hardware is not limited to an ISA and allows for implementing fast, wide, and custom datapaths with extremely short iteration times.

## Slide 14: GCD Algorithms Comparison
Algorithm
[DdPM+21]
[BY19]
[Por20]
Our work
GCD-preserving Transformation
a
Worst-Case Iterations
387 *
1548 *
384
1542
vs
* Two-bit PM [YZ86]
1X difference for 255 bits
1X difference for 1024 bits
Stein [Ste67]
Euclid (300 BC)
Notes: A 2X difference is not large, why not in software?
Intuition is division is faster, software do not seem to do two-bit PM
Could be faster in software
Multiple subtractions
Two-bit in software
Is subtraction twice as fast as divison?
We extend the two-bit PM algorithm for extended GCD
We observed all hardware papers built from efficient algorithms chosen in efficient software implementations. We look at if this is optimal.
Iteration time = Longest series of data-dependent operations
Since software is constrained to using instructions predefined in the processor’s instruction set architecture (ISA), software iteration times correspond to the longest set of dependent instructions. In contrast, hardware is not limited to an ISA and allows for implementing fast, wide, and custom datapaths with extremely short iteration times.

## Slide 15: GCD Algorithms Comparison
Algorithm
[DdPM+21]
[BY19]
[Por20]
Our work
GCD-preserving Transformation
a
Worst-Case Iterations
Average Iterations
387 *
1548 *
300 *
1195 *
384
1542
189
598
vs
* Two-bit PM [YZ86]
1X difference for 255 bits
1X difference for 1024 bits
1.6X difference for 255 bits
2X difference for 1024 bits
Stein [Ste67]
Euclid (300 BC)
Notes: A 2X difference is not large, why not in software?
Intuition is division is faster, software do not seem to do two-bit PM
Could be faster in software
Multiple subtractions
Two-bit in software
Is subtraction twice as fast as divison?
We extend the two-bit PM algorithm for extended GCD
We observed all hardware papers built from efficient algorithms chosen in efficient software implementations. We look at if this is optimal.
Iteration time = Longest series of data-dependent operations
Since software is constrained to using instructions predefined in the processor’s instruction set architecture (ISA), software iteration times correspond to the longest set of dependent instructions. In contrast, hardware is not limited to an ISA and allows for implementing fast, wide, and custom datapaths with extremely short iteration times.

## Slide 16: From GCD to Extended GCD (XGCD)
Compute Bézout coefficients satisfying Bézout Identity
Maintain these relations each cycle, where
Notes: Extension is computing these coefficients b_a and b_b
GCD is 1, interesting result is finding these coefficients
  Start: and
  End:
Extension is computing these coefficients b_a and b_b
GCD is 1, interesting result is finding these coefficients
  Start: 𝑢=1,𝑚=0 and 𝑦=0, 𝑛=1
  End: gcd⁡(𝑎_0,𝑏_0 )=𝑎, 𝑏_𝑎=𝑢, 𝑏_𝑏=𝑚

## Slide 17: Two-bit PM Critical Path
GCD update:
XGCD update:
Notes: May not be clear…
(details in paper)
Bring back time here?

## Slide 18: Euclid critical path
Compute
Compute
Get MSBs
LUT
Compute
Notes: Most quotients in Euclid’s algorithm are small for 1024-bit inputs
Can estimate few of the most significant bits of for faster execution
HW block diagram
LUT -> computes q * b -> stacked adders with partial products
Compute remainder goes into another adder
Most quotients in Euclid’s algorithm are small for 1024-bit inputs
Can estimate few of the most significant bits of 𝑞 for faster execution
HW block diagram
LUT -> computes q * b -> stacked adders with partial products
Compute remainder goes into another adder

## Slide 19: Euclid critical path
Computing the remainder
Compute
Compute
Compute
Get MSBs
LUT
Multiplier
Notes: HW block diagram
LUT -> computes q * b -> stacked adders with partial products
Compute remainder goes into another adder

## Slide 20: Euclid critical path
Computing the remainder
Compute
Compute
Compute
Get MSBs
LUT
Multiplier
Notes: HW block diagram
LUT -> computes q * b -> stacked adders with partial products
Compute remainder goes into another adder

## Slide 21: Critical paths primarily require additions
The fastest adder is a carry-save adder (CSA)
  Eliminates carry propagation, requiring delay
  Stores numbers in CSA form or redundant binary form
1 1 1 0
1 1 0 1 (a)
1 1 1 0 (b)
0 0 1 0 (c)
----------------
1 1 1 0 1
1 1 0 1 (a)
1 1 1 0 (b)
0 0 1 0 (c)
-------------------
0 0 0 1 sum
1 1 1 0 0 carry
-------------------
1 1 1 0 1
Notes: Both critical paths require additions
  Two-bit PM adds
  Euclid requires multiplying , which adds partial products, and subtracts to get the remainder
Both critical paths require additions
  Two-bit PM adds 𝑢 + 𝑦 + 3𝐵
  Euclid requires multiplying 𝑞∗𝑏, which adds partial products, and subtracts 𝑎−𝑞∗𝑏 to get the remainder

## Slide 22: Two-bit PM critical path: 3 CSA delays
CSA
CSA
CSA
CSA
CSA
CSA
CSA
CSA
CSA
w
Data with bitwidth w
Notes: Shift is nontrivial

## Slide 23: Euclid critical path
Compute
Compute
Compute
Get MSBs
LUT
Require 6-bit normal adds to get MSBs of
CSA delays
Notes: HW block diagram
LUT -> computes q * b -> stacked adders with partial products
Compute remainder goes into another adder

## Slide 24: Euclid critical path: at least 9 CSA delays
Compute
Compute
Compute
Computing the remainder
Get MSBs
LUT
Multiplier
Add 14 values with CSAs CSA delays
Require 6-bit normal adds to get MSBs of
CSA delays
Notes: HW block diagram
LUT -> computes q * b -> stacked adders with partial products
Compute remainder goes into another adder

## Slide 25: Two-bit PM is a faster starting point
Two-bit PM critical path is at least 3X shorter than Euclid’s
Two-bit PM iteration counts are at most 2X higher than Euclid’s
Two-bit PM with carry-save adders is the more promising starting point for hardware in the average and the worst-case.

## Slide 26: Our unified design with constant-time config
[DdPM+21]
[BY19]
[Por20]
Our work
Approach
Termination Condition
Pad to worst-case cycle count
Cycle count equal to worst case
Reduce inputs until GCD
or
vs
CT
NCT
Application Requirements
Note that since are in CSA form, we do not know when they become
Notes: Constant-power?

## Slide 27: We focus on the optimal design space
Software
NCT
CT
NCT
CT
Hardware
NCT
CT
Target Platform
Algorithm
Application Requirements
[AHAJS16]
[ZST+20]
[ZTW21]
[DdPM+21]
[BY19]
[Por20]
CT = constant-time, NCT = not constant-time
Unified
Our work

## Slide 28: Accelerator Execution
Pre-processing
Post-processing
Iterations Loop
(until termination condition is satisfied)
4 cycles
8 cycles
Worst-case 1548 cycles for 1024-bit inputs and 387 cycles for 255-bit inputs
Execution Time

## Slide 29: Accelerator Execution
Iterations Loop
(until termination condition is satisfied)
4 cycles
8 cycles
Worst-case 1548 cycles for 1024-bit inputs and 387 cycles for 255-bit inputs
Execution Time
Preserve results when shifting in CSA form
Pre-processing
Post-processing

## Slide 30: Accelerator Execution
Iterations Loop
(until termination condition is satisfied)
4 cycles
8 cycles
Worst-case 1548 cycles for 1024-bit inputs and 387 cycles for 255-bit inputs
Execution Time
Preserve results when shifting in CSA form
Allocate multiple cycles for processing steps
Pre-processing
Post-processing

## Slide 31: Accelerator Execution
Iterations Loop
(until termination condition is satisfied)
4 cycles
8 cycles
Worst-case 1548 cycles for 1024-bit inputs and 387 cycles for 255-bit inputs
Execution Time
Preserve results when shifting in CSA form
Allocate multiple cycles for processing steps
Subsample for termination condition
Pre-processing
Post-processing

## Slide 32: Accelerator Execution
Iterations Loop
(until termination condition is satisfied)
4 cycles
8 cycles
Worst-case 1548 cycles for 1024-bit inputs and 387 cycles for 255-bit inputs
Execution Time
Preserve results when shifting in CSA form
Allocate multiple cycles for processing steps
Subsample for termination condition
Minimize control overhead
Pre-processing
Post-processing

## Slide 33: Critical Path for ASIC in 16nm
 | 255-bit XGCD | 1024-bit XGCD
DFF clk to Q | 45 | 40
Inverter | 7 | 0
CSA | 18 | 39
CSA | 31 | 39
Buffer | 13 | 0
CSA | 30 | 34
Shift in CSA form | 15 | 18
Late select muxes | 18 | 18
Precomputing control | 27 | 22
Setup Time | 2 | 5
Total | 204 | 215
Notes: Sums are the same up until clock skew
Clock skew definition
- Different bitwidths: critical paths are same
however, build a chip -> smaller 255 -> longer wires -> clock skew
Physical design -> contributor to difference
Ideal versions of circuits = same clock speed
Physical limitation
Critical path is what we expected
Different bitwidths
Clock skew

## Slide 34: Critical Path for ASIC in 16nm
 | 255-bit XGCD | 1024-bit XGCD
DFF clk to Q | 45 | 40
Inverter | 7 | 0
CSA | 18 | 39
CSA | 31 | 39
Buffer | 13 | 0
CSA | 30 | 34
Shift in CSA form | 15 | 18
Late select muxes | 18 | 18
Precomputing control | 27 | 22
Setup Time | 2 | 5
Clock Skew | 16 | 41
Total | 220 | 257
These are post-layout numbers for a fabrication-ready design
Notes: Sums are the same up until clock skew
Clock skew definition
- Different bitwidths: critical paths are same
however, build a chip -> smaller 255 -> longer wires -> clock skew
Physical design -> contributor to difference
Ideal versions of circuits = same clock speed
Physical limitation
Critical path is what we expected
Different bitwidths
Clock skew

## Slide 35: 255-bit Constant-time XGCD Comparison
Chart: 
| 2.2999999999999998 | 2.2999999999999998 | 0.20699999999999999 | 0.44700000000000001 | 4.55
Cycles | 8543 | 6253 | 8466 | 386 | 386
Clock Frequency (GHz)
100
105
103
104
102
101
Cycle Count
[BY19]: 3.7
[Por20]: 2.7
[DdPM+21]: 41
Better
Ours: 0.089
* Times are in us
Our ASIC
31X faster than [Por20]
First for constant-time 255-bit XGCD
Software
FPGA
ASIC

## Slide 36: 255-bit Constant-time XGCD Comparison
Chart: 
| 2.2999999999999998 | 2.2999999999999998 | 0.20699999999999999 | 0.44700000000000001 | 4.55
Cycles | 8543 | 6253 | 8466 | 386 | 386
Clock Frequency (GHz)
100
105
103
104
102
101
Cycle Count
[BY19]: 3.7
[Por20]: 2.7
[DdPM+21]: 41
Better
Ours: 0.089
Ours: 0.902
* Times are in us
Our ASIC
31X faster than [Por20]
First for constant-time 255-bit XGCD
Direct FPGA Comparison
Our design is 45X faster
Software
FPGA
ASIC

## Slide 37: 1024-bit XGCD Comparison
Our ASIC
36X faster than software
8X faster than state-of-the-art ASIC
Clock Frequency (GHz)
100
105
103
104
102
101
Cycle Count
Better
Chart: 
| 3.9940000000000003E-2 | 0.248 | 0.25 | 0.5 | 3.89 | 1
Cycles | 598 | 1143 | 1623 | 3000 | 1143 | 10650
[ZTW21]: 6.5
[AHAJS16]: 15
[ZST+20]: 6
Ours: 0.295
* Times are in us
GNU C++ on Apple M1: 10.7
Software
FPGA
ASIC
Notes: Technology-scaled for ASIC comparison

## Slide 38: 1024-bit XGCD Comparison
Our ASIC
36X faster than software
8X faster than state-of-the-art ASIC
Direct FPGA Comparison
Our design is 2.7X faster
Clock Frequency (GHz)
100
105
103
104
102
101
Cycle Count
Better
Chart: 
| 3.9940000000000003E-2 | 0.248 | 0.25 | 0.5 | 3.89 | 1
Cycles | 598 | 1143 | 1623 | 3000 | 1143 | 10650
[ZTW21]: 6.5
[AHAJS16]: 15
[ZST+20]: 6
Ours: 5.6
Ours: 0.295
* Times are in us
GNU C++ on Apple M1: 10.7
Software
FPGA
ASIC

## Slide 39: Our design impacts application approaches
Supports progression in state of the art for Curve25519
Notes: Exponentiation mod p
Fixed exp, variable base
Check if in multiplicative subgroup
Fastest possible multiplication algorithm for fixed exponent
Addition chains (current state of the art)
1.5 * n -> ops
Addition-subtraction chain (generalization) -> sum/diff between two prior values in chain
Divisions instead of multiplications for exponentiation mod p

## Slide 40: Our design impacts application approaches
Supports progression in state of the art for Curve25519
Informs reasonable security levels for this type of VDF
Notes: Exponentiation mod p
Fixed exp, variable base
Check if in multiplicative subgroup
Fastest possible multiplication algorithm for fixed exponent
Addition chains (current state of the art)
1.5 * n -> ops
Addition-subtraction chain (generalization) -> sum/diff between two prior values in chain
Divisions instead of multiplications for exponentiation mod p

## Slide 41: Our design impacts application approaches
Supports progression in state of the art for Curve25519
Informs reasonable security levels for this type of VDF
May be useful for other applications
Notes: Exponentiation mod p
Fixed exp, variable base
Check if in multiplicative subgroup
Fastest possible multiplication algorithm for fixed exponent
Addition chains (current state of the art)
1.5 * n -> ops
Addition-subtraction chain (generalization) -> sum/diff between two prior values in chain
Divisions instead of multiplications for exponentiation mod p

## Slide 42: Our design impacts application approaches
Supports progression in state of the art for Curve25519
Informs reasonable security levels for this type of VDF
May be useful for other applications
https://github.com/kavyasreedhar/sreedhar-xgcd-hardware-ches2022
Notes: Exponentiation mod p
Fixed exp, variable base
Check if in multiplicative subgroup
Fastest possible multiplication algorithm for fixed exponent
Addition chains (current state of the art)
1.5 * n -> ops
Addition-subtraction chain (generalization) -> sum/diff between two prior values in chain
Divisions instead of multiplications for exponentiation mod p

## Slide 43: A Fast Large-Integer Extended GCD Algorithm and Hardware Design for Verifiable Delay Functions and Modular Inversion
Kavya Sreedhar, Mark Horowitz, Christopher Torng
Stanford University
skavya@stanford.edu
September 19, 2022

## Slide 44: Extended GCD
Computes Bézout coefficients satisfying Bézout’s Identity
Notes: Fundamental operation in number

## Slide 45: Extended GCD is widely used in cryptography
Computes Bézout coefficients satisfying Bézout’s Identity
Modular Multiplicative Inverse
RSA
Elliptic Curve Cryptography
ElGamal Encryption
.
.
.
Notes: Lot of work in 1980s, 1990s
Efficient software implementations

## Slide 46: There is an increasing need for faster XGCD
Modular Inversion for Curve25519 [Ber06]
  Constant-time XGCD faster than Fermat’s Little Theorem [BY19]
Notes: Much larger bitwidths, chia uses 1024-bit switches every 10 minutes
91% of execution time

## Slide 47: There is an increasing need for faster XGCD
Modular Inversion for Curve25519 [Ber06]
  Constant-time XGCD faster than Fermat’s Little Theorem [BY19]
Squaring binary quadratic forms over class groups [Wes19] as a VDF
  XGCD is the bottleneck
in a class group
[BBBF18]
Notes: Much larger bitwidths, chia uses 1024-bit switches every 10 minutes
91% of execution time

## Slide 48: There is an increasing need for faster XGCD
Modular Inversion for Curve25519 [Ber06]
  Constant-time XGCD faster than Fermat’s Little Theorem [BY19]
Squaring binary quadratic forms over class groups [Wes19] as a VDF
  XGCD is the bottleneck
in a class group
255-bits, constant-time
1024-bits, not constant-time
[BBBF18]
Notes: Much larger bitwidths, chia uses 1024-bit switches every 10 minutes
91% of execution time

## Slide 49
Chart: 
| 2.2999999999999998 | 2.2999999999999998 | 0.20699999999999999 | 0.44700000000000001 | 4.55
Cycles | 8543 | 6253 | 8466 | 386 | 386
Clock Frequency (GHz)
255-bit constant-time XGCD
100
105
103
104
102
101
Cycle Count
[BY19]
[Por20]
[DdPM+21]
Better
No ASIC points
Software
FPGA
ASIC
Notes: Legend
No ASIC points, state of the art is 2X faster
- Bold arrow that says better for lower right
Prototypes on FPGAs, we also did a prototype on FPGA and showed improvement
Axis, lines = execution time, faster slower
Not that many papers
ASIC – no ASIC 255-bit, 2x faster in 1024-bit
Not only are there not that many papers, transition

## Slide 50
Chart: 
| 2.2999999999999998 | 2.2999999999999998 | 0.20699999999999999 | 0.44700000000000001 | 4.55
Cycles | 8543 | 6253 | 8466 | 386 | 386
Chart: 
| 3.9940000000000003E-2 | 0.248 | 0.25 | 0.5 | 3.89 | 1
Cycles | 598 | 1143 | 1623 | 3000 | 1143 | 10650
Clock Frequency (GHz)
Clock Frequency (GHz)
1024-bit XGCD
255-bit constant-time XGCD
100
105
103
104
102
101
Cycle Count
[BY19]
[Por20]
[DdPM+21]
[ZTW21]
[AHAJS16]
[ZST+20]
Better
Better
No ASIC points
[ZST+20] is 2X faster than C++
Software
FPGA
ASIC
GNU C++ on Apple M1
Notes: Legend
No ASIC points, state of the art is 2X faster
- Bold arrow that says better for lower right
Prototypes on FPGAs, we also did a prototype on FPGA and showed improvement
Axis, lines = execution time, faster slower
Not that many papers
ASIC – no ASIC 255-bit, 2x faster in 1024-bit
Not only are there not that many papers, transition

## Slide 51: Current view of XGCD design space
Hardware
NCT
CT
Target Platform
Algorithm
Application Requirements
[AHAJS16]
[ZST+20]
[ZTW21]
[DdPM+21]
CT = constant-time, NCT = not constant-time
Notes: Focus on division
All these prior works provide point solutions to improve either average performance (for squaring binary quadratic forms) or worst-case performance (for constant-time applications). They also all build from Euclid’s algorithm, citing its low iteration count and efficient software implementations.

## Slide 52: We explore the broader design space
Software
NCT
CT
NCT
CT
Hardware
NCT
CT
NCT
CT
Target Platform
Algorithm
Application Requirements
[AHAJS16]
[ZST+20]
[ZTW21]
[DdPM+21]
[BY19]
[Por20]
CT = constant-time, NCT = not constant-time
Notes: From software to hardware
Iterative algorithms

## Slide 53: We explore the broader design space
Software
NCT
CT
NCT
CT
Hardware
NCT
CT
Target Platform
Algorithm
Application Requirements
[AHAJS16]
[ZST+20]
[ZTW21]
[DdPM+21]
[BY19]
[Por20]
CT = constant-time, NCT = not constant-time
Unified
Our work
Notes: From software to hardware

## Slide 54: Hardware allows for short iteration times
Target Platform
[DdPM+21]
[BY19]
[Por20]
Our work
Number of Iterations
Constrained to ISA
From algorithm
Yes
From algorithm
No
Execution time = number of iterations iteration time
The control over iteration time in hardware opens the opportunity to accelerate simpler algorithms that require more iterations.
vs
Software
Hardware
Notes: Critical Path determines clock period, which 1 over the frequency
We observed all hardware papers built from efficient algorithms chosen in efficient software implementations. We look at if this is optimal.
Iteration time = Longest series of data-dependent operations
Since software is constrained to using instructions predefined in the processor’s instruction set architecture (ISA), software iteration times correspond to the longest set of dependent instructions. In contrast, hardware is not limited to an ISA and allows for implementing fast, wide, and custom datapaths with extremely short iteration times.
We can complete an iteration at frequencies equal to or higher than frequencies of processors
Unlike prior work

## Slide 55: GCD Algorithms Comparison
Algorithm
[DdPM+21]
[BY19]
[Por20]
Our work
GCD-preserving Transformation
a
vs
Stein [Ste67]
Euclid (300 BC)
Notes: A 2X difference is not large, why not in software?
Intuition is division is faster, software do not seem to do two-bit PM
Could be faster in software
Multiple subtractions
Two-bit in software
Is subtraction twice as fast as divison?
We extend the two-bit PM algorithm for extended GCD
We observed all hardware papers built from efficient algorithms chosen in efficient software implementations. We look at if this is optimal.
Iteration time = Longest series of data-dependent operations
Since software is constrained to using instructions predefined in the processor’s instruction set architecture (ISA), software iteration times correspond to the longest set of dependent instructions. In contrast, hardware is not limited to an ISA and allows for implementing fast, wide, and custom datapaths with extremely short iteration times.

## Slide 56: GCD Algorithms Comparison
Algorithm
[DdPM+21]
[BY19]
[Por20]
Our work
GCD-preserving Transformation
a
Worst-Case Iterations
387 *
1548 *
384
1542
vs
* Two-bit PM [YZ86]
1X difference for 255 bits
1X difference for 1024 bits
Stein [Ste67]
Euclid (300 BC)
Notes: A 2X difference is not large, why not in software?
Intuition is division is faster, software do not seem to do two-bit PM
Could be faster in software
Multiple subtractions
Two-bit in software
Is subtraction twice as fast as divison?
We extend the two-bit PM algorithm for extended GCD
We observed all hardware papers built from efficient algorithms chosen in efficient software implementations. We look at if this is optimal.
Iteration time = Longest series of data-dependent operations
Since software is constrained to using instructions predefined in the processor’s instruction set architecture (ISA), software iteration times correspond to the longest set of dependent instructions. In contrast, hardware is not limited to an ISA and allows for implementing fast, wide, and custom datapaths with extremely short iteration times.

## Slide 57: GCD Algorithms Comparison
Algorithm
[DdPM+21]
[BY19]
[Por20]
Our work
GCD-preserving Transformation
a
Worst-Case Iterations
Average Iterations
387 *
1548 *
300 *
1195 *
384
1542
189
598
vs
* Two-bit PM [YZ86]
1X difference for 255 bits
1X difference for 1024 bits
1.6X difference for 255 bits
2X difference for 1024 bits
Stein [Ste67]
Euclid (300 BC)
Notes: A 2X difference is not large, why not in software?
Intuition is division is faster, software do not seem to do two-bit PM
Could be faster in software
Multiple subtractions
Two-bit in software
Is subtraction twice as fast as divison?
We extend the two-bit PM algorithm for extended GCD
We observed all hardware papers built from efficient algorithms chosen in efficient software implementations. We look at if this is optimal.
Iteration time = Longest series of data-dependent operations
Since software is constrained to using instructions predefined in the processor’s instruction set architecture (ISA), software iteration times correspond to the longest set of dependent instructions. In contrast, hardware is not limited to an ISA and allows for implementing fast, wide, and custom datapaths with extremely short iteration times.

## Slide 58: GCD to XGCD
Compute Bézout coefficients satisfying Bézout Identity
Maintain these relations each cycle, where
Notes: Extension is computing these coefficients b_a and b_b
GCD is 1, interesting result is finding these coefficients
  Start: and
  End:
Extension is computing these coefficients b_a and b_b
GCD is 1, interesting result is finding these coefficients
  Start: 𝑢=1,𝑚=0 and 𝑦=0, 𝑛=1
  End: gcd⁡(𝑎_0,𝑏_0 )=𝑎, 𝑏_𝑎=𝑢, 𝑏_𝑏=𝑚

## Slide 59: Two-bit PM Critical Path
GCD update:
Add odd constant when divisibility of does not match that of
XGCD update:
Notes: May not be clear…
(details in paper)
Bring back time here?

## Slide 60: Euclid critical path
Compute
Compute
Get MSBs
LUT
Compute
Notes: Most quotients in Euclid’s algorithm are small for 1024-bit inputs
Can estimate few of the most significant bits of for faster execution
HW block diagram
LUT -> computes q * b -> stacked adders with partial products
Compute remainder goes into another adder
Most quotients in Euclid’s algorithm are small for 1024-bit inputs
Can estimate few of the most significant bits of 𝑞 for faster execution
HW block diagram
LUT -> computes q * b -> stacked adders with partial products
Compute remainder goes into another adder

## Slide 61: Euclid critical path
Computing the remainder
Compute
Compute
Compute
Get MSBs
LUT
Multiplier
Notes: HW block diagram
LUT -> computes q * b -> stacked adders with partial products
Compute remainder goes into another adder

## Slide 62: Euclid critical path
Computing the remainder
Compute
Compute
Compute
Get MSBs
LUT
Multiplier
Notes: HW block diagram
LUT -> computes q * b -> stacked adders with partial products
Compute remainder goes into another adder

## Slide 63: Critical paths primarily require additions
The fastest adder is a carry-save adder (CSA)
  Eliminates carry propagation, requiring delay
  Stores numbers in CSA form or redundant binary form
1 1 1 0
1 1 0 1 (a)
1 1 1 0 (b)
0 0 1 0 (c)
----------------
1 1 1 0 1
1 1 0 1 (a)
1 1 1 0 (b)
0 0 1 0 (c)
-------------------
0 0 0 1 sum
1 1 1 0 0 carry
-------------------
1 1 1 0 1
Notes: Both critical paths require additions
  Two-bit PM adds
  Euclid requires multiplying , which adds partial products, and subtracts to get the remainder
Both critical paths require additions
  Two-bit PM adds 𝑢 + 𝑦 + 3𝐵
  Euclid requires multiplying 𝑞∗𝑏, which adds partial products, and subtracts 𝑎−𝑞∗𝑏 to get the remainder

## Slide 64: Two-bit PM critical path: 3 CSA delays
CSA
CSA
CSA
Notes: Shift is nontrivial

## Slide 65: Euclid critical path
Compute
Compute
Compute
Get MSBs
LUT
Require 6-bit normal adds to get MSBs of
CSA delays
Notes: HW block diagram
LUT -> computes q * b -> stacked adders with partial products
Compute remainder goes into another adder

## Slide 66: Euclid critical path: 9 CSA delays
Compute
Compute
Compute
Computing the remainder
Get MSBs
LUT
Multiplier
Add 14 values with CSAs CSA delays
Require 6-bit normal adds to get MSBs of
CSA delays
Notes: HW block diagram
LUT -> computes q * b -> stacked adders with partial products
Compute remainder goes into another adder

## Slide 67: Two-bit PM is a faster starting point
Two-bit PM critical path is at least 3X shorter than Euclid’s
Two-bit PM iteration counts are at most 2X higher than Euclid’s
Two-bit PM with carry-save adders is the more promising starting point for hardware in the average and the worst-case.

## Slide 68: Our unified design with constant-time config
[DdPM+21]
[BY19]
[Por20]
Our work
Approach
Termination Condition
Pad to worst-case cycle count
Cycle count equal to worst case
Reduce inputs until GCD
or
vs
CT
NCT
Application Requirements
Note that since are in CSA form, we do not know when they become
Notes: Constant-power?

## Slide 69: We focus on the optimal design space
Software
NCT
CT
NCT
CT
Hardware
NCT
CT
Target Platform
Algorithm
Application Requirements
[AHAJS16]
[ZST+20]
[ZTW21]
[DdPM+21]
[BY19]
[Por20]
CT = constant-time, NCT = not constant-time
Unified
Our work

## Slide 70: Accelerator Execution
Pre-processing
Post-processing
Iterations Loop
(until termination condition is satisfied)
4 cycles
8 cycles
Worst-case 1548 cycles for 1024-bit inputs and 386 cycles for 255-bit inputs
Execution Time

## Slide 71: Accelerator Execution
Pre-processing
Post-processing
Iterations Loop
(until termination condition is satisfied)
4 cycles
8 cycles
Worst-case 1548 cycles for 1024-bit inputs and 386 cycles for 255-bit inputs
Execution Time
Preserve results when shifting in CSA form

## Slide 72: Accelerator Execution
Pre-processing
Post-processing
Iterations Loop
(until termination condition is satisfied)
4 cycles
8 cycles
Worst-case 1548 cycles for 1024-bit inputs and 386 cycles for 255-bit inputs
Execution Time
Preserve results when shifting in CSA form
Allocate multiple cycles for processing steps

## Slide 73: Accelerator Execution
Pre-processing
Post-processing
Iterations Loop
(until termination condition is satisfied)
4 cycles
8 cycles
Worst-case 1548 cycles for 1024-bit inputs and 386 cycles for 255-bit inputs
Execution Time
Preserve results when shifting in CSA form
Allocate multiple cycles for processing steps
Subsample for termination condition

## Slide 74: Accelerator Execution
Pre-processing
Post-processing
Iterations Loop
(until termination condition is satisfied)
4 cycles
8 cycles
Worst-case 1548 cycles for 1024-bit inputs and 386 cycles for 255-bit inputs
Execution Time
Preserve results when shifting in CSA form
Allocate multiple cycles for processing steps
Subsample for termination condition
Minimize control overhead

## Slide 75: Critical Path for ASIC in 16nm
 | 255-bit XGCD | 1024-bit XGCD
DFF clk to Q | 45 | 40
Inverter | 7 | 0
CSA | 18 | 39
CSA | 31 | 39
Buffer | 13 | 0
CSA | 30 | 34
Shift in CSA form | 15 | 18
Late select muxes | 18 | 18
Precomputing control | 27 | 22
Setup Time | 2 | 5
Total | 204 | 215
Notes: Sums are the same up until clock skew
Clock skew definition
- Different bitwidths: critical paths are same
however, build a chip -> smaller 255 -> longer wires -> clock skew
Physical design -> contributor to difference
Ideal versions of circuits = same clock speed
Physical limitation
Critical path is what we expected
Different bitwidths
Clock skew

## Slide 76: Critical Path for ASIC in 16nm
 | 255-bit XGCD | 1024-bit XGCD
DFF clk to Q | 45 | 40
Inverter | 7 | 0
CSA | 18 | 39
CSA | 31 | 39
Buffer | 13 | 0
CSA | 30 | 34
Shift in CSA form | 15 | 18
Late select muxes | 18 | 18
Precomputing control | 27 | 22
Setup Time | 2 | 5
Clock Skew | 16 | 41
Total | 220 | 257
We are taping out the 255-bit and 1279-bit versions of this design in GF12 this month
Notes: Sums are the same up until clock skew
Clock skew definition
- Different bitwidths: critical paths are same
however, build a chip -> smaller 255 -> longer wires -> clock skew
Physical design -> contributor to difference
Ideal versions of circuits = same clock speed
Physical limitation
Critical path is what we expected
Different bitwidths
Clock skew

## Slide 77: 255-bit Constant-time XGCD Comparison
Chart: 
| 2.2999999999999998 | 2.2999999999999998 | 0.20699999999999999 | 0.44700000000000001 | 4.55
Cycles | 8543 | 6253 | 8466 | 386 | 386
Clock Frequency (GHz)
100
105
103
104
102
101
Cycle Count
[BY19]: 3.7
[Por20]: 2.7
[DdPM+21]: 41
Better
Ours: 0.085
* Times are in us
Our ASIC
32X faster than [Por20]
First for constant-time 255-bit XGCD
Software
FPGA
ASIC

## Slide 78: 255-bit Constant-time XGCD Comparison
Chart: 
| 2.2999999999999998 | 2.2999999999999998 | 0.20699999999999999 | 0.44700000000000001 | 4.55
Cycles | 8543 | 6253 | 8466 | 386 | 386
Clock Frequency (GHz)
100
105
103
104
102
101
Cycle Count
[BY19]: 3.7
[Por20]: 2.7
[DdPM+21]: 41
Better
Ours: 0.085
Ours: 0.863
* Times are in us
Our ASIC
32X faster than [Por20]
First for constant-time 255-bit XGCD
Direct FPGA Comparison
Our design is 48X faster
Software
FPGA
ASIC

## Slide 79: 1024-bit XGCD Comparison
Our ASIC
36X faster than software
8X faster than state-of-the-art ASIC
Clock Frequency (GHz)
100
105
103
104
102
101
Cycle Count
Better
Chart: 
| 3.9940000000000003E-2 | 0.248 | 0.25 | 0.5 | 3.89 | 1
Cycles | 598 | 1143 | 1623 | 3000 | 1143 | 10650
[ZTW21]: 6.5
[AHAJS16]: 15
[ZST+20]: 6
Ours: 0.294
* Times are in us
GNU C++ on Apple M1: 10.7
Software
FPGA
ASIC

## Slide 80: 1024-bit XGCD Comparison
Our ASIC
36X faster than software
8X faster than state-of-the-art ASIC
Direct FPGA Comparison
Our design is 3X faster
Clock Frequency (GHz)
100
105
103
104
102
101
Cycle Count
Better
Chart: 
| 3.9940000000000003E-2 | 0.248 | 0.25 | 0.5 | 3.89 | 1
Cycles | 598 | 1143 | 1623 | 3000 | 1143 | 10650
[ZTW21]: 6.5
[AHAJS16]: 15
[ZST+20]: 6
Ours: 4.6
Ours: 0.294
* Times are in us
GNU C++ on Apple M1: 10.7
Software
FPGA
ASIC

## Slide 81: Our design impacts application approaches
Supports progression in state of the art for Curve25519
  To point multiplication algorithms that use more inversions
Notes: Exponentiation mod p
Fixed exp, variable base
Check if in multiplicative subgroup
Fastest possible multiplication algorithm for fixed exponent
Addition chains (current state of the art)
1.5 * n -> ops
Addition-subtraction chain (generalization) -> sum/diff between two prior values in chain
Divisions instead of multiplications for exponentiation mod p

## Slide 82: Our design impacts application approaches
Supports progression in state of the art for Curve25519
  To point multiplication algorithms that use more inversions
Informs reasonable security levels for this type of VDF
  Since our XGCD hardware is 36X faster than software
Notes: Exponentiation mod p
Fixed exp, variable base
Check if in multiplicative subgroup
Fastest possible multiplication algorithm for fixed exponent
Addition chains (current state of the art)
1.5 * n -> ops
Addition-subtraction chain (generalization) -> sum/diff between two prior values in chain
Divisions instead of multiplications for exponentiation mod p

## Slide 83: Our design impacts application approaches
Supports progression in state of the art for Curve25519
  To point multiplication algorithms that use more inversions
Informs reasonable security levels for this type of VDF
  Since our hardware is 30 to 40X faster than software
May be useful for other applications?
Notes: Exponentiation mod p
Fixed exp, variable base
Check if in multiplicative subgroup
Fastest possible multiplication algorithm for fixed exponent
Addition chains (current state of the art)
1.5 * n -> ops
Addition-subtraction chain (generalization) -> sum/diff between two prior values in chain
Divisions instead of multiplications for exponentiation mod p

## Slide 84: Our design impacts application approaches
Supports progression in state of the art for Curve25519
  To point multiplication algorithms that use more inversions
Informs reasonable security levels for this type of VDF
  Since our hardware is 30 to 40X faster than software
May be useful for other applications?
https://github.com/kavyasreedhar/sreedhar-xgcd-hardware-ches2022
Notes: Exponentiation mod p
Fixed exp, variable base
Check if in multiplicative subgroup
Fastest possible multiplication algorithm for fixed exponent
Addition chains (current state of the art)
1.5 * n -> ops
Addition-subtraction chain (generalization) -> sum/diff between two prior values in chain
Divisions instead of multiplications for exponentiation mod p

## Slide 85: A Fast Large-Integer Extended GCD Algorithm and Hardware Design for Verifiable Delay Functions and Modular Inversion
Kavya Sreedhar, Mark Horowitz, Christopher Torng
Stanford University
skavya@stanford.edu
September 19, 2022

## Slide 86: Extended GCD
Computes Bézout coefficients satisfying Bézout’s Identity
Notes: Fundamental operation in number

## Slide 87: Extended GCD is widely used in cryptography
Computes Bézout coefficients satisfying Bézout’s Identity
Modular Multiplicative Inverse
RSA
Elliptic Curve Cryptography
ElGamal Encryption
.
.
.
Notes: Lot of work in 1980s, 1990s
Efficient software implementations

## Slide 88: There is an increasing need for faster XGCD
Modular Inversion for Curve25519 [Ber06]
  Constant-time XGCD faster than Fermat’s Little Theorem [BY19]
Notes: Bernstein yang CHES

## Slide 89: There is an increasing need for faster XGCD
Modular Inversion for Curve25519 [Ber06]
  Constant-time XGCD faster than Fermat’s Little Theorem [BY19]
Squaring binary quadratic forms over class groups [Wes19]
  As a VDF [BBBF18]
  XGCD is the bottleneck
Notes: Much larger bitwidths, chia uses 1024-bit switches every 10 minutes
91% of execution time

## Slide 90
Chart: 
| 2.2999999999999998 | 2.2999999999999998 | 0.20699999999999999 | 0.44700000000000001 | 4.55
Cycles | 8543 | 6253 | 8466 | 386 | 386
Clock Frequency (GHz)
255-bit constant-time XGCD
100
105
103
104
102
101
Cycle Count
[BY19]
[Por20]
[DdPM+21]
Better
No ASIC points
Software
FPGA
ASIC
Notes: Legend
No ASIC points, state of the art is 2X faster
- Bold arrow that says better for lower right
Prototypes on FPGAs, we also did a prototype on FPGA and showed improvement
Axis, lines = execution time, faster slower
Not that many papers
ASIC – no ASIC 255-bit, 2x faster in 1024-bit
Not only are there not that many papers, transition

## Slide 91
Chart: 
| 2.2999999999999998 | 2.2999999999999998 | 0.20699999999999999 | 0.44700000000000001 | 4.55
Cycles | 8543 | 6253 | 8466 | 386 | 386
Chart: 
| 3.9940000000000003E-2 | 0.248 | 0.25 | 0.5 | 3.89 | 1
Cycles | 598 | 1143 | 1623 | 3000 | 1143 | 10650
Clock Frequency (GHz)
Clock Frequency (GHz)
1024-bit XGCD
255-bit constant-time XGCD
100
105
103
104
102
101
Cycle Count
[BY19]
[Por20]
[DdPM+21]
[ZTW21]
[AHAJS16]
[ZST+20]
Better
Better
No ASIC points
[ZST+20] is 2X faster than C++
Software
FPGA
ASIC
GNU C++ on Apple M1
Notes: Legend
No ASIC points, state of the art is 2X faster
- Bold arrow that says better for lower right
Prototypes on FPGAs, we also did a prototype on FPGA and showed improvement
Axis, lines = execution time, faster slower
Not that many papers
ASIC – no ASIC 255-bit, 2x faster in 1024-bit
Not only are there not that many papers, transition

## Slide 92: Current view of XGCD design space
Hardware
NCT
CT
Target Platform
Algorithm
Application Requirements
[AHAJS16]
[ZST+20]
[ZTW21]
[DdPM+21]
CT = constant-time, NCT = not constant-time
Notes: Focus on division
All these prior works provide point solutions to improve either average performance (for squaring binary quadratic forms) or worst-case performance (for constant-time applications). They also all build from Euclid’s algorithm, citing its low iteration count and efficient software implementations.

## Slide 93: We explore the broader design space
Software
NCT
CT
NCT
CT
Hardware
NCT
CT
NCT
CT
Target Platform
Algorithm
Application Requirements
[AHAJS16]
[ZST+20]
[ZTW21]
[DdPM+21]
[BY19]
[Por20]
CT = constant-time, NCT = not constant-time
Notes: From software to hardware
Iterative algorithms

## Slide 94: We explore the broader design space
Software
NCT
CT
NCT
CT
Hardware
NCT
CT
Target Platform
Algorithm
Application Requirements
[AHAJS16]
[ZST+20]
[ZTW21]
[DdPM+21]
[BY19]
[Por20]
CT = constant-time, NCT = not constant-time
Unified
Our work
Notes: From software to hardware

## Slide 95: Hardware allows for short iteration times
Target Platform
[DdPM+21]
[BY19]
[Por20]
Our work
Number of Iterations
Constrained to ISA
From algorithm
Yes
From algorithm
No
Execution time = number of iterations iteration time
The control over iteration time in hardware opens the opportunity to accelerate simpler algorithms that require more iterations.
vs
Software
Hardware
Notes: Critical Path determines clock period, which 1 over the frequency
We observed all hardware papers built from efficient algorithms chosen in efficient software implementations. We look at if this is optimal.
Iteration time = Longest series of data-dependent operations
Since software is constrained to using instructions predefined in the processor’s instruction set architecture (ISA), software iteration times correspond to the longest set of dependent instructions. In contrast, hardware is not limited to an ISA and allows for implementing fast, wide, and custom datapaths with extremely short iteration times.
We can complete an iteration at frequencies equal to or higher than frequencies of processors
Unlike prior work

## Slide 96: GCD Algorithms Comparison
Algorithm
[DdPM+21]
[BY19]
[Por20]
Our work
GCD-preserving Transformation
a
vs
* Two-bit PM [YZ86]
Stein
Euclid
Notes: A 2X difference is not large, why not in software?
Intuition is division is faster, software do not seem to do two-bit PM
Could be faster in software
Multiple subtractions
Two-bit in software
Is subtraction twice as fast as divison?
We extend the two-bit PM algorithm for extended GCD
We observed all hardware papers built from efficient algorithms chosen in efficient software implementations. We look at if this is optimal.
Iteration time = Longest series of data-dependent operations
Since software is constrained to using instructions predefined in the processor’s instruction set architecture (ISA), software iteration times correspond to the longest set of dependent instructions. In contrast, hardware is not limited to an ISA and allows for implementing fast, wide, and custom datapaths with extremely short iteration times.

## Slide 97: GCD Algorithms Comparison
Algorithm
[DdPM+21]
[BY19]
[Por20]
Our work
GCD-preserving Transformation
a
Worst-Case Iterations
387 *
1548 *
384
1542
vs
* Two-bit PM [YZ86]
Stein
Euclid
1X difference for 255 bits
1X difference for 1024 bits
Notes: A 2X difference is not large, why not in software?
Intuition is division is faster, software do not seem to do two-bit PM
Could be faster in software
Multiple subtractions
Two-bit in software
Is subtraction twice as fast as divison?
We extend the two-bit PM algorithm for extended GCD
We observed all hardware papers built from efficient algorithms chosen in efficient software implementations. We look at if this is optimal.
Iteration time = Longest series of data-dependent operations
Since software is constrained to using instructions predefined in the processor’s instruction set architecture (ISA), software iteration times correspond to the longest set of dependent instructions. In contrast, hardware is not limited to an ISA and allows for implementing fast, wide, and custom datapaths with extremely short iteration times.

## Slide 98: GCD Algorithms Comparison
Algorithm
[DdPM+21]
[BY19]
[Por20]
Our work
GCD-preserving Transformation
a
Worst-Case Iterations
Average Iterations
387 *
1548 *
300 *
1195 *
384
1542
189
598
vs
* Two-bit PM [YZ86]
Stein
Euclid
1X difference for 255 bits
1X difference for 1024 bits
1.6X difference for 255 bits
2X difference for 1024 bits
Notes: A 2X difference is not large, why not in software?
Intuition is division is faster, software do not seem to do two-bit PM
Could be faster in software
Multiple subtractions
Two-bit in software
Is subtraction twice as fast as divison?
We extend the two-bit PM algorithm for extended GCD
We observed all hardware papers built from efficient algorithms chosen in efficient software implementations. We look at if this is optimal.
Iteration time = Longest series of data-dependent operations
Since software is constrained to using instructions predefined in the processor’s instruction set architecture (ISA), software iteration times correspond to the longest set of dependent instructions. In contrast, hardware is not limited to an ISA and allows for implementing fast, wide, and custom datapaths with extremely short iteration times.

## Slide 99: GCD to XGCD
Compute Bézout coefficients satisfying Bézout Identity
Maintain these relations each cycle, where
Notes: Extension is computing these coefficients b_a and b_b
GCD is 1, interesting result is finding these coefficients
  Start: and
  End:
Extension is computing these coefficients b_a and b_b
GCD is 1, interesting result is finding these coefficients
  Start: 𝑢=1,𝑚=0 and 𝑦=0, 𝑛=1
  End: gcd⁡(𝑎_0,𝑏_0 )=𝑎, 𝑏_𝑎=𝑢, 𝑏_𝑏=𝑚

## Slide 100: Two-bit PM Critical Path
GCD update:
Add odd constant when divisibility of does not match that of
XGCD update:
Notes: May not be clear…
(details in paper)
Bring back time here?

## Slide 101: Euclid critical path
Compute
Compute
Get MSBs
LUT
Compute
Notes: Most quotients in Euclid’s algorithm are small for 1024-bit inputs
Can estimate few of the most significant bits of for faster execution
HW block diagram
LUT -> computes q * b -> stacked adders with partial products
Compute remainder goes into another adder
Most quotients in Euclid’s algorithm are small for 1024-bit inputs
Can estimate few of the most significant bits of 𝑞 for faster execution
HW block diagram
LUT -> computes q * b -> stacked adders with partial products
Compute remainder goes into another adder

## Slide 102: Euclid critical path
Computing the remainder
Compute
Compute
Compute
Get MSBs
LUT
Multiplier
Notes: HW block diagram
LUT -> computes q * b -> stacked adders with partial products
Compute remainder goes into another adder

## Slide 103: Euclid critical path
Computing the remainder
Compute
Compute
Compute
Get MSBs
LUT
Multiplier
Notes: HW block diagram
LUT -> computes q * b -> stacked adders with partial products
Compute remainder goes into another adder

## Slide 104: Critical paths primarily require additions
The fastest adder is a carry-save adder (CSA)
  Eliminates carry propagation, requiring delay
  Stores numbers in CSA form or redundant binary form
1 1 1 0
1 1 0 1 (a)
1 1 1 0 (b)
0 0 1 0 (c)
----------------
1 1 1 0 1
1 1 0 1 (a)
1 1 1 0 (b)
0 0 1 0 (c)
-------------------
0 0 0 1 sum
1 1 1 0 0 carry
-------------------
1 1 1 0 1
Notes: Both critical paths require additions
  Two-bit PM adds
  Euclid requires multiplying , which adds partial products, and subtracts to get the remainder
Both critical paths require additions
  Two-bit PM adds 𝑢 + 𝑦 + 3𝐵
  Euclid requires multiplying 𝑞∗𝑏, which adds partial products, and subtracts 𝑎−𝑞∗𝑏 to get the remainder

## Slide 105: Two-bit PM with 3:2 CSAs: 3 CSA Delays
CSA
CSA
CSA
Notes: Shift is nontrivial

## Slide 106: Euclid with CSAs
Compute
Compute
Compute
Get MSBs
LUT
Require 6-bit normal adds to get MSBs of
CSA delays
Notes: HW block diagram
LUT -> computes q * b -> stacked adders with partial products
Compute remainder goes into another adder

## Slide 107: Euclid with CSAs: 9 CSA delays
Compute
Compute
Compute
Computing the remainder
Get MSBs
LUT
Multiplier
Add 14 values with CSAs CSA delays
Require 6-bit normal adds to get MSBs of
CSA delays
Notes: HW block diagram
LUT -> computes q * b -> stacked adders with partial products
Compute remainder goes into another adder

## Slide 108: Two-bit PM is a faster starting point
Two-bit PM critical path is at least 3X shorter than Euclid’s
Two-bit PM iteration counts are at most 2X higher than Euclid’s
Two-bit PM with carry-save adders is the more promising starting point for hardware in the average and the worst-case.

## Slide 109: Our unified design with constant-time config
[DdPM+21]
[BY19]
[Por20]
Our work
Approach
Termination Condition
Pad to worst-case cycle count
Cycle count equal to worst case
Reduce inputs until GCD
or
vs
CT
NCT
Application Requirements
Note that since are in CSA form, we do not know when they become
Notes: Constant-power?

## Slide 110: We focus on the optimal design space
Software
NCT
CT
NCT
CT
Hardware
NCT
CT
Target Platform
Algorithm
Application Requirements
[AHAJS16]
[ZST+20]
[ZTW21]
[DdPM+21]
[BY19]
[Por20]
CT = constant-time, NCT = not constant-time
Unified
Our work

## Slide 111: Accelerator Execution

## Slide 112: Accelerator Execution

## Slide 113: Accelerator Execution
Preserve results when shifting in CSA form

## Slide 114: Accelerator Execution
Preserve results when shifting in CSA form
Allocate multiple cycles for processing steps

## Slide 115: Accelerator Execution
Preserve results when shifting in CSA form
Allocate multiple cycles for processing steps
Subsample for termination condition

## Slide 116: Accelerator Execution
Preserve results when shifting in CSA form
Allocate multiple cycles for processing steps
Subsample for termination condition
Minimize control overhead

## Slide 117: Critical Path in 16nm
 | 255-bit XGCD | 1024-bit XGCD
DFF clk to Q | 45 | 40
Inverter | 7 | 0
CSA | 18 | 39
CSA | 31 | 39
Buffer | 13 | 0
CSA | 30 | 34
Shift in CSA form | 15 | 18
Late select muxes | 18 | 18
Precomputing control | 27 | 22
Setup Time | 2 | 5
Clock Skew | 16 | 41
Total | 220 | 257
Notes: Sums are the same up until clock skew
Clock skew definition
- Different bitwidths: critical paths are same
however, build a chip -> smaller 255 -> longer wires -> clock skew
Physical design -> contributor to difference
Ideal versions of circuits = same clock speed
Physical limitation
Critical path is what we expected
Different bitwidths
Clock skew

## Slide 118: 255-bit Constant-time XGCD Comparison
Chart: 
| 2.2999999999999998 | 2.2999999999999998 | 0.20699999999999999 | 0.44700000000000001 | 4.55
Cycles | 8543 | 6253 | 8466 | 386 | 386
Clock Frequency (GHz)
100
105
103
104
102
101
Cycle Count
[BY19]: 3.7
[Por20]: 2.7
[DdPM+21]: 41
Better
Ours: 0.085
* Times are in us
Our ASIC
32X faster than [Por20]
First for constant-time 255-bit XGCD
Software
FPGA
ASIC

## Slide 119: 255-bit Constant-time XGCD Comparison
Chart: 
| 2.2999999999999998 | 2.2999999999999998 | 0.20699999999999999 | 0.44700000000000001 | 4.55
Cycles | 8543 | 6253 | 8466 | 386 | 386
Clock Frequency (GHz)
100
105
103
104
102
101
Cycle Count
[BY19]: 3.7
[Por20]: 2.7
[DdPM+21]: 41
Better
Ours: 0.085
Ours: 0.863
* Times are in us
Our ASIC
32X faster than [Por20]
First for constant-time 255-bit XGCD
Direct FPGA Comparison
Our design is 48X faster
Software
FPGA
ASIC

## Slide 120: 1024-bit XGCD Comparison
Our ASIC
36X faster than software
8X faster than state-of-the-art ASIC
Clock Frequency (GHz)
100
105
103
104
102
101
Cycle Count
Better
Chart: 
| 3.9940000000000003E-2 | 0.248 | 0.25 | 0.5 | 3.89 | 1
Cycles | 598 | 1143 | 1623 | 3000 | 1143 | 10650
[ZTW21]: 6.5
[AHAJS16]: 15
[ZST+20]: 6
Ours: 0.294
* Times are in us
GNU C++ on Apple M1: 10.7
Software
FPGA
ASIC

## Slide 121: 1024-bit XGCD Comparison
Our ASIC
36X faster than software
8X faster than state-of-the-art ASIC
Direct FPGA Comparison
Our design is 3X faster
Clock Frequency (GHz)
100
105
103
104
102
101
Cycle Count
Better
Chart: 
| 3.9940000000000003E-2 | 0.248 | 0.25 | 0.5 | 3.89 | 1
Cycles | 598 | 1143 | 1623 | 3000 | 1143 | 10650
[ZTW21]: 6.5
[AHAJS16]: 15
[ZST+20]: 6
Ours: 4.6
Ours: 0.294
* Times are in us
GNU C++ on Apple M1: 10.7
Software
FPGA
ASIC

## Slide 122: Our design impacts application approaches
Supports progression in state of the art for Curve25519
  To point multiplication algorithms that use more inversions
Notes: Exponentiation mod p
Fixed exp, variable base
Check if in multiplicative subgroup
Fastest possible multiplication algorithm for fixed exponent
Addition chains (current state of the art)
1.5 * n -> ops
Addition-subtraction chain (generalization) -> sum/diff between two prior values in chain
Divisions instead of multiplications for exponentiation mod p

## Slide 123: Our design impacts application approaches
Supports progression in state of the art for Curve25519
  To point multiplication algorithms that use more inversions
Informs reasonable security levels for this type of VDF
  Since our hardware is 30 to 40X faster than software
Notes: Exponentiation mod p
Fixed exp, variable base
Check if in multiplicative subgroup
Fastest possible multiplication algorithm for fixed exponent
Addition chains (current state of the art)
1.5 * n -> ops
Addition-subtraction chain (generalization) -> sum/diff between two prior values in chain
Divisions instead of multiplications for exponentiation mod p

## Slide 124: Our design impacts application approaches
Supports progression in state of the art for Curve25519
  To point multiplication algorithms that use more inversions
Informs reasonable security levels for this type of VDF
  Since our hardware is 30 to 40X faster than software
May be useful for other applications?
Notes: Exponentiation mod p
Fixed exp, variable base
Check if in multiplicative subgroup
Fastest possible multiplication algorithm for fixed exponent
Addition chains (current state of the art)
1.5 * n -> ops
Addition-subtraction chain (generalization) -> sum/diff between two prior values in chain
Divisions instead of multiplications for exponentiation mod p

## Slide 125: Our design impacts application approaches
Supports progression in state of the art for Curve25519
  To point multiplication algorithms that use more inversions
Informs reasonable security levels for this type of VDF
  Since our hardware is 30 to 40X faster than software
May be useful for other applications?
https://github.com/kavyasreedhar/sreedhar-xgcd-hardware-ches2022
Notes: Exponentiation mod p
Fixed exp, variable base
Check if in multiplicative subgroup
Fastest possible multiplication algorithm for fixed exponent
Addition chains (current state of the art)
1.5 * n -> ops
Addition-subtraction chain (generalization) -> sum/diff between two prior values in chain
Divisions instead of multiplications for exponentiation mod p

## Slide 126: A Fast Large-Integer Extended GCD Algorithm and Hardware Design for Verifiable Delay Functions and Modular Inversion
Kavya Sreedhar, Mark Horowitz, Christopher Torng
Stanford University
skavya@stanford.edu
September 19, 2022

## Slide 127: Extended GCD
Computes Bézout coefficients satisfying Bézout’s Identity
Notes: Fundamental operation in number

## Slide 128: Extended GCD is widely used in cryptography
Computes Bézout coefficients satisfying Bézout’s Identity
Modular Multiplicative Inverse
RSA
Elliptic Curve Cryptography
ElGamal Encryption
.
.
.
Notes: Lot of work in 1980s, 1990s
Efficient software implementations

## Slide 129: There is an increasing need for faster XGCD
Modular Inversion for Curve25519 [Ber06]
  Constant-time XGCD faster than Fermat’s Little Theorem [BY19]
Notes: Bernstein yang CHES

## Slide 130: There is an increasing need for faster XGCD
Modular Inversion for Curve25519 [Ber06]
  Constant-time XGCD faster than Fermat’s Little Theorem [BY19]
Squaring binary quadratic forms over class groups [Wes19]
  As a VDF [BBBF18]
  XGCD is the bottleneck
Notes: Much larger bitwidths, chia uses 1024-bit switches every 10 minutes
91% of execution time

## Slide 131
Chart: 
| 2.2999999999999998 | 2.2999999999999998 | 0.20699999999999999 | 0.44700000000000001 | 4.55
Cycles | 8543 | 6253 | 8466 | 386 | 386
Clock Frequency (GHz)
255-bit constant-time XGCD
100
105
103
104
102
101
Cycle Count
[BY19]
[Por20]
[DdPM+21]
Better
No ASIC points
Software
FPGA
ASIC
Notes: Legend
No ASIC points, state of the art is 2X faster
- Bold arrow that says better for lower right
Prototypes on FPGAs, we also did a prototype on FPGA and showed improvement
Axis, lines = execution time, faster slower
Not that many papers
ASIC – no ASIC 255-bit, 2x faster in 1024-bit
Not only are there not that many papers, transition

## Slide 132
Chart: 
| 2.2999999999999998 | 2.2999999999999998 | 0.20699999999999999 | 0.44700000000000001 | 4.55
Cycles | 8543 | 6253 | 8466 | 386 | 386
Chart: 
| 3.9940000000000003E-2 | 0.248 | 0.25 | 0.5 | 3.89 | 1
Cycles | 598 | 1143 | 1623 | 3000 | 1143 | 10650
Clock Frequency (GHz)
Clock Frequency (GHz)
1024-bit XGCD
255-bit constant-time XGCD
100
105
103
104
102
101
Cycle Count
[BY19]
[Por20]
[DdPM+21]
[ZTW21]
[AHAJS16]
[ZST+20]
Better
Better
No ASIC points
[ZST+20] is 2X faster than C++
Software
FPGA
ASIC
Notes: Legend
No ASIC points, state of the art is 2X faster
- Bold arrow that says better for lower right
Prototypes on FPGAs, we also did a prototype on FPGA and showed improvement
Axis, lines = execution time, faster slower
Not that many papers
ASIC – no ASIC 255-bit, 2x faster in 1024-bit
Not only are there not that many papers, transition

## Slide 133: Current view of XGCD design space
Hardware
NCT
CT
Target Platform
Algorithm
Application Requirements
[AHAJS16]
[ZST+20]
[ZTW21]
[DdPM+21]
CT = constant-time, NCT = not constant-time
Notes: Focus on division
All these prior works provide point solutions to improve either average performance (for squaring binary quadratic forms) or worst-case performance (for constant-time applications). They also all build from Euclid’s algorithm, citing its low iteration count and efficient software implementations.

## Slide 134: We explore the broader design space
Software
NCT
CT
NCT
CT
Hardware
NCT
CT
NCT
CT
Target Platform
Algorithm
Application Requirements
[AHAJS16]
[ZST+20]
[ZTW21]
[DdPM+21]
[BY19]
[Por20]
CT = constant-time, NCT = not constant-time
Notes: From software to hardware
Iterative algorithms

## Slide 135: We explore the broader design space
Software
NCT
CT
NCT
CT
Hardware
NCT
CT
Target Platform
Algorithm
Application Requirements
[AHAJS16]
[ZST+20]
[ZTW21]
[DdPM+21]
[BY19]
[Por20]
CT = constant-time, NCT = not constant-time
Unified
Our work
Notes: From software to hardware

## Slide 136: Hardware allows for short iteration times
Target Platform
[DdPM+21]
[BY19]
[Por20]
Our work
Number of Iterations
Constrained to ISA
From algorithm
Yes
From algorithm
No
Execution time = number of iterations iteration time
The control over iteration time in hardware opens the opportunity to accelerate simpler algorithms that require more iterations.
vs
Software
Hardware
Notes: Critical Path determines clock period, which 1 over the frequency
We observed all hardware papers built from efficient algorithms chosen in efficient software implementations. We look at if this is optimal.
Iteration time = Longest series of data-dependent operations
Since software is constrained to using instructions predefined in the processor’s instruction set architecture (ISA), software iteration times correspond to the longest set of dependent instructions. In contrast, hardware is not limited to an ISA and allows for implementing fast, wide, and custom datapaths with extremely short iteration times.
We can complete an iteration at frequencies equal to or higher than frequencies of processors
Unlike prior work

## Slide 137: GCD Algorithms Comparison
Algorithm
[DdPM+21]
[BY19]
[Por20]
Our work
GCD-preserving Transformation
a
vs
Stein
Euclid
Notes: A 2X difference is not large, why not in software?
Intuition is division is faster, software do not seem to do two-bit PM
Could be faster in software
Multiple subtractions
Two-bit in software
Is subtraction twice as fast as divison?
We extend the two-bit PM algorithm for extended GCD
We observed all hardware papers built from efficient algorithms chosen in efficient software implementations. We look at if this is optimal.
Iteration time = Longest series of data-dependent operations
Since software is constrained to using instructions predefined in the processor’s instruction set architecture (ISA), software iteration times correspond to the longest set of dependent instructions. In contrast, hardware is not limited to an ISA and allows for implementing fast, wide, and custom datapaths with extremely short iteration times.

## Slide 138: GCD Algorithms Comparison
Algorithm
[DdPM+21]
[BY19]
[Por20]
Our work
GCD-preserving Transformation
a
Worst-Case Iterations
387 *
1548 *
384
1542
vs
* Two-bit PM [YZ86]
Stein
Euclid
1X for 255-bit to 1024-bit inputs
Notes: A 2X difference is not large, why not in software?
Intuition is division is faster, software do not seem to do two-bit PM
Could be faster in software
Multiple subtractions
Two-bit in software
Is subtraction twice as fast as divison?
We extend the two-bit PM algorithm for extended GCD
We observed all hardware papers built from efficient algorithms chosen in efficient software implementations. We look at if this is optimal.
Iteration time = Longest series of data-dependent operations
Since software is constrained to using instructions predefined in the processor’s instruction set architecture (ISA), software iteration times correspond to the longest set of dependent instructions. In contrast, hardware is not limited to an ISA and allows for implementing fast, wide, and custom datapaths with extremely short iteration times.

## Slide 139: GCD Algorithms Comparison
Algorithm
[DdPM+21]
[BY19]
[Por20]
Our work
GCD-preserving Transformation
a
Worst-Case Iterations
Average Iterations
387 *
1548 *
300 *
1195 *
384
1542
189
598
vs
* Two-bit PM [YZ86]
Stein
Euclid
1X for 255-bit to 1024-bit inputs
1.6X to 2X for 255-bit to 1024-bit inputs
Notes: A 2X difference is not large, why not in software?
Intuition is division is faster, software do not seem to do two-bit PM
Could be faster in software
Multiple subtractions
Two-bit in software
Is subtraction twice as fast as divison?
We extend the two-bit PM algorithm for extended GCD
We observed all hardware papers built from efficient algorithms chosen in efficient software implementations. We look at if this is optimal.
Iteration time = Longest series of data-dependent operations
Since software is constrained to using instructions predefined in the processor’s instruction set architecture (ISA), software iteration times correspond to the longest set of dependent instructions. In contrast, hardware is not limited to an ISA and allows for implementing fast, wide, and custom datapaths with extremely short iteration times.

## Slide 140: GCD to XGCD
Compute Bézout coefficients satisfying Bézout Identity
Maintain these relations each cycle, where
Notes: Extension is computing these coefficients b_a and b_b
GCD is 1, interesting result is finding these coefficients
  Start: and
  End:
Extension is computing these coefficients b_a and b_b
GCD is 1, interesting result is finding these coefficients
  Start: 𝑢=1,𝑚=0 and 𝑦=0, 𝑛=1
  End: gcd⁡(𝑎_0,𝑏_0 )=𝑎, 𝑏_𝑎=𝑢, 𝑏_𝑏=𝑚

## Slide 141: Two-bit PM Critical Path
GCD update:
Add odd constant when divisibility of does not match that of
XGCD update:
Notes: May not be clear…
(details in paper)
Bring back time here?

## Slide 142: Euclid critical path
Compute
Compute
Get MSBs
LUT
Compute
Notes: Most quotients in Euclid’s algorithm are small for 1024-bit inputs
Can estimate few of the most significant bits of for faster execution
HW block diagram
LUT -> computes q * b -> stacked adders with partial products
Compute remainder goes into another adder
Most quotients in Euclid’s algorithm are small for 1024-bit inputs
Can estimate few of the most significant bits of 𝑞 for faster execution
HW block diagram
LUT -> computes q * b -> stacked adders with partial products
Compute remainder goes into another adder

## Slide 143: Euclid critical path
Computing the remainder
Compute
Compute
Compute
Get MSBs
LUT
Multiplier
Notes: HW block diagram
LUT -> computes q * b -> stacked adders with partial products
Compute remainder goes into another adder

## Slide 144: Euclid critical path
Computing the remainder
Compute
Compute
Compute
Get MSBs
LUT
Multiplier
Notes: HW block diagram
LUT -> computes q * b -> stacked adders with partial products
Compute remainder goes into another adder

## Slide 145: Critical paths primarily require additions
The fastest adder is a carry-save adder (CSA)
  Eliminates carry propagation, requiring delay
  Stores numbers in CSA form or redundant binary form
1 1 1 0
1 1 0 1 (a)
1 1 1 0 (b)
0 0 1 0 (c)
----------------
1 1 1 0 1
1 1 0 1 (a)
1 1 1 0 (b)
0 0 1 0 (c)
-------------------
0 0 0 1 sum
1 1 1 0 0 carry
-------------------
1 1 1 0 1
Notes: Both critical paths require additions
  Two-bit PM adds
  Euclid requires multiplying , which adds partial products, and subtracts to get the remainder
Both critical paths require additions
  Two-bit PM adds 𝑢 + 𝑦 + 3𝐵
  Euclid requires multiplying 𝑞∗𝑏, which adds partial products, and subtracts 𝑎−𝑞∗𝑏 to get the remainder

## Slide 146: Two-bit PM with 3:2 CSAs: 3 CSA Delays
CSA
CSA
CSA
Notes: Shift is nontrivial

## Slide 147: Euclid with CSAs
Compute
Compute
Compute
Get MSBs
LUT
Require 6-bit normal adds to get MSBs of
CSA delays
Notes: HW block diagram
LUT -> computes q * b -> stacked adders with partial products
Compute remainder goes into another adder

## Slide 148: Euclid with CSAs: 9 CSA delays
Compute
Compute
Compute
Computing the remainder
Get MSBs
LUT
Multiplier
Add 14 values with CSAs CSA delays
Require 6-bit normal adds to get MSBs of
CSA delays
Notes: HW block diagram
LUT -> computes q * b -> stacked adders with partial products
Compute remainder goes into another adder

## Slide 149: Two-bit PM is a faster starting point
Two-bit PM critical path is at least 3X shorter than Euclid’s
Two-bit PM iteration counts are at most 2X higher than Euclid’s
Two-bit PM with carry-save adders is the more promising starting point for hardware in the average and the worst-case.

## Slide 150: Our unified design with constant-time config
[DdPM+21]
[BY19]
[Por20]
Our work
Approach
Termination Condition
Pad to worst-case cycle count
Cycle count equal to worst case
Reduce inputs until GCD
or
vs
CT
NCT
Application Requirements
Note that since are in CSA form, we do not know when they become
Notes: Constant-power?

## Slide 151: We focus on the optimal design space
Software
NCT
CT
NCT
CT
Hardware
NCT
CT
Target Platform
Algorithm
Application Requirements
[AHAJS16]
[ZST+20]
[ZTW21]
[DdPM+21]
[BY19]
[Por20]
CT = constant-time, NCT = not constant-time
Unified
Our work

## Slide 152: Is three-bit PM faster in hardware?
Yes, for average case execution
  Reduce three bits when are even

## Slide 153: Is three-bit PM faster in hardware?
Yes, for average case execution
  Reduce three bits when are even
No, for constant-time execution
  Reduce one bit when are even

## Slide 154: Accelerator Execution Flow

## Slide 155: Processing steps do not limit clock frequency

## Slide 156: Shifting in CSA form for variable updates
Preserve sign
Correct truncated results

## Slide 157: Minimizing control overhead
Parallel computation + late selects
Precompute control signals

## Slide 158: Termination condition subsamples

## Slide 159: Critical Path in 16nm
 | 1024-bit XGCD | 255-bit XGCD
DFF clk to Q | 45 | 40
Inverter | 7 | 0
CSA | 18 | 39
CSA | 31 | 39
Buffer | 13 | 0
CSA | 30 | 34
Shift in CSA form | 15 | 18
Late select muxes | 18 | 18
Precomputing control | 27 | 22
Setup Time | 2 | 5
Clock Skew | 16 | 41
Total | 220 | 257
Notes: Sums are the same up until clock skew
Clock skew definition
- Different bitwidths: critical paths are same
however, build a chip -> smaller 255 -> longer wires -> clock skew
Physical design -> contributor to difference
Ideal versions of circuits = same clock speed
Physical limitation
Critical path is what we expected
Different bitwidths
Clock skew

## Slide 160: 255-bit Constant-time XGCD Comparison
Chart: 
| 2.2999999999999998 | 2.2999999999999998 | 0.20699999999999999 | 0.44700000000000001 | 4.55
Cycles | 8543 | 6253 | 8466 | 386 | 386
Clock Frequency (GHz)
100
105
103
104
102
101
Cycle Count
[BY19]: 3.7
[Por20]: 2.7
[DdPM+21]: 41
Better
Ours: 0.085
Ours: 0.863
* Times are in us
Our ASIC
32X faster than [Por20]
First for constant-time 255-bit XGCD
Direct FPGA Comparison
Our design is 48X faster
Software
FPGA
ASIC

## Slide 161: 1024-bit XGCD Comparison
Our ASIC
36X faster than software
8X faster than state-of-the-art ASIC
Direct FPGA Comparison
Our design is 3X faster
Clock Frequency (GHz)
100
105
103
104
102
101
Cycle Count
Better
Chart: 
| 3.9940000000000003E-2 | 0.248 | 0.25 | 0.5 | 3.89 | 1
Cycles | 598 | 1143 | 1623 | 3000 | 1143 | 10650
[ZTW21]: 6.5
[AHAJS16]: 15
[ZST+20]: 6
Ours: 4.6
Ours: 0.294
* Times are in us
GNU C++ on Apple M1: 10.7
Software
FPGA
ASIC

## Slide 162: Our design impacts application approaches
Supports progression in state of the art for Curve25519
  To point multiplication algorithms that use more inversions
Notes: Exponentiation mod p
Fixed exp, variable base
Check if in multiplicative subgroup
Fastest possible multiplication algorithm for fixed exponent
Addition chains (current state of the art)
1.5 * n -> ops
Addition-subtraction chain (generalization) -> sum/diff between two prior values in chain
Divisions instead of multiplications for exponentiation mod p

## Slide 163: Our design impacts application approaches
Supports progression in state of the art for Curve25519
  To point multiplication algorithms that use more inversions
Informs reasonable security levels for this type of VDF
  Since our hardware is 30 to 40X faster than software
Notes: Exponentiation mod p
Fixed exp, variable base
Check if in multiplicative subgroup
Fastest possible multiplication algorithm for fixed exponent
Addition chains (current state of the art)
1.5 * n -> ops
Addition-subtraction chain (generalization) -> sum/diff between two prior values in chain
Divisions instead of multiplications for exponentiation mod p

## Slide 164: Our design impacts application approaches
Supports progression in state of the art for Curve25519
  To point multiplication algorithms that use more inversions
Informs reasonable security levels for this type of VDF
  Since our hardware is 30 to 40X faster than software
May be useful for other applications?
Notes: Exponentiation mod p
Fixed exp, variable base
Check if in multiplicative subgroup
Fastest possible multiplication algorithm for fixed exponent
Addition chains (current state of the art)
1.5 * n -> ops
Addition-subtraction chain (generalization) -> sum/diff between two prior values in chain
Divisions instead of multiplications for exponentiation mod p

## Slide 165: Our design impacts application approaches
Supports progression in state of the art for Curve25519
  To point multiplication algorithms that use more inversions
Informs reasonable security levels for this type of VDF
  Since our hardware is 30 to 40X faster than software
May be useful for other applications?
https://github.com/kavyasreedhar/sreedhar-xgcd-hardware-ches2022
Notes: Exponentiation mod p
Fixed exp, variable base
Check if in multiplicative subgroup
Fastest possible multiplication algorithm for fixed exponent
Addition chains (current state of the art)
1.5 * n -> ops
Addition-subtraction chain (generalization) -> sum/diff between two prior values in chain
Divisions instead of multiplications for exponentiation mod p

## Slide 166: A Fast Large-Integer Extended GCD Algorithm and Hardware Design for Verifiable Delay Functions and Modular Inversion
Kavya Sreedhar, Mark Horowitz, Christopher Torng
Stanford University
skavya@stanford.edu
September 19, 2022

## Slide 167: Extended GCD
Computes Bézout coefficients satisfying Bézout’s Identity

## Slide 168: Extended GCD is widely used in cryptography
Computes Bézout coefficients satisfying Bézout’s Identity
Modular Multiplicative Inverse
RSA
Elliptic Curve Cryptography
ElGamal Encryption
.
.
.
Notes: Lot of work in 1980s, 1990s
Efficient software implementations

## Slide 169: There is an increasing need for faster XGCD
Modular Inversion for Curve25519 [Ber06]
  Constant-time XGCD faster than Fermat’s Little Theorem [BY19]
Notes: Bernstein yang CHES

## Slide 170: There is an increasing need for faster XGCD
Modular Inversion for Curve25519 [Ber06]
  Constant-time XGCD faster than Fermat’s Little Theorem [BY19]
Squaring binary quadratic forms over class groups [Wes19]
  As a VDF [BBBF18]
  XGCD is the bottleneck
Notes: Much larger bitwidths, chia uses 1024-bit switches every 10 minutes
91% of execution time

## Slide 171: How fast can one do XGCD?
Chart: 255-bit constant-time XGCD
| 2.2999999999999998 | 2.2999999999999998
Software | 8543 | 6253
FPGA | 8466
No ASIC points

## Slide 172: How fast can one do XGCD?
Chart: 255-bit constant-time XGCD
| 2.2999999999999998 | 2.2999999999999998
Software | 8543 | 6253
FPGA | 8466
No ASIC points
Chart: 1024-bit XGCD
| 3.9940000000000003E-2
FPGA | 598
ASIC | 1623 | 3000
[ZST+20] 2x faster than C++
GNU C++ on Apple M1
Notes: - Bold arrow that says better for lower right
Prototypes on FPGAs, we also did a prototype on FPGA and showed improvement
Axis, lines = execution time, faster slower
Not that many papers
ASIC – no ASIC 255-bit, 2x faster in 1024-bit
Not only are there not that many papers, transition

## Slide 173: Current view of XGCD design space
Hardware
NCT
CT
Target Platform
Algorithm
Application Requirements
[AHAJS16]
[ZST+20]
[ZTW21]
[DdPM+21]
CT = constant-time, NCT = not constant-time
Notes: Focus on division
All these prior works provide point solutions to improve either average performance (for squaring binary quadratic forms) or worst-case performance (for constant-time applications). They also all build from Euclid’s algorithm, citing its low iteration count and efficient software implementations.

## Slide 174: We explore the broader design space
Software
NCT
CT
NCT
CT
Hardware
NCT
CT
NCT
CT
Target Platform
Algorithm
Application Requirements
[AHAJS16]
[ZST+20]
[ZTW21]
[DdPM+21]
[BY19]
[Por20]
CT = constant-time, NCT = not constant-time
Notes: From software to hardware
Iterative algorithms

## Slide 175: We explore the broader design space
Software
NCT
CT
NCT
CT
Hardware
NCT
CT
Target Platform
Algorithm
Application Requirements
[AHAJS16]
[ZST+20]
[ZTW21]
[DdPM+21]
[BY19]
[Por20]
CT = constant-time, NCT = not constant-time
Unified
Our work
Notes: From software to hardware

## Slide 176: Hardware allows for short iteration times
Target Platform
[DdPM+21]
[BY19]
[Por20]
Our work
Number of Iterations
Constrained to ISA
From algorithm
Yes
From algorithm
No
Execution time = number of iterations iteration time
The control over iteration time in hardware opens the opportunity to accelerate simpler algorithms that require more iterations.
vs
Software
Hardware
Notes: Critical Path determines clock period, which 1 over the frequency
We observed all hardware papers built from efficient algorithms chosen in efficient software implementations. We look at if this is optimal.
Iteration time = Longest series of data-dependent operations
Since software is constrained to using instructions predefined in the processor’s instruction set architecture (ISA), software iteration times correspond to the longest set of dependent instructions. In contrast, hardware is not limited to an ISA and allows for implementing fast, wide, and custom datapaths with extremely short iteration times.
We can complete an iteration at frequencies equal to or higher than frequencies of processors
Unlike prior work

## Slide 177: GCD Algorithms Comparison
Algorithm
[BY19]
[Por20]
Iterative Operation
GCD-preserving Transformation
Subtraction (Base: Stein)
Division (Base: Euclid)
vs
Notes: Shifts when are even
Two-bit PM algorithm reduces a factor
Shifts when 𝑎,𝑏 are even
Two-bit PM algorithm reduces a factor

## Slide 178: GCD Algorithms Comparison
Algorithm
[DdPM+21]
[BY19]
[Por20]
Our work
Iterative Operation
GCD-preserving Transformation
Worst-Case Iterations
Subtraction (Base: Stein)
387 *
Division (Base: Euclid)
384
vs
for 255-bit inputs
1X
* [YZ86]
Notes: list average and worst-case iterations for both
Subtraction is faster for constant-time XGCD
We observed all hardware papers built from efficient algorithms chosen in efficient software implementations. We look at if this is optimal.
Iteration time = Longest series of data-dependent operations
Since software is constrained to using instructions predefined in the processor’s instruction set architecture (ISA), software iteration times correspond to the longest set of dependent instructions. In contrast, hardware is not limited to an ISA and allows for implementing fast, wide, and custom datapaths with extremely short iteration times.

## Slide 179: GCD Algorithms Comparison
Algorithm
[DdPM+21]
[BY19]
[Por20]
Our work
Iterative Operation
GCD-preserving Transformation
Worst-Case Iterations
Average Iterations
Subtraction (Base: Stein)
387 *
1195 *
Division (Base: Euclid)
384
598
vs
for 255-bit inputs
1X
for 1024-bit inputs
2X
* [YZ86]
Notes: A 2X difference is not large, why not in software?
Intuition is division is faster, software do not seem to do two-bit PM
Could be faster in software
Multiple subtractions
Two-bit in software
Is subtraction twice as fast as divison?
We extend the two-bit PM algorithm for extended GCD
We observed all hardware papers built from efficient algorithms chosen in efficient software implementations. We look at if this is optimal.
Iteration time = Longest series of data-dependent operations
Since software is constrained to using instructions predefined in the processor’s instruction set architecture (ISA), software iteration times correspond to the longest set of dependent instructions. In contrast, hardware is not limited to an ISA and allows for implementing fast, wide, and custom datapaths with extremely short iteration times.

## Slide 180: GCD to XGCD
Compute Bézout coefficients satisfying Bézout Identity
Maintain these relations each cycle, where
Notes: Extension is computing these coefficients b_a and b_b
GCD is 1, interesting result is finding these coefficients
  Start: and
  End:
Extension is computing these coefficients b_a and b_b
GCD is 1, interesting result is finding these coefficients
  Start: 𝑢=1,𝑚=0 and 𝑦=0, 𝑛=1
  End: gcd⁡(𝑎_0,𝑏_0 )=𝑎, 𝑏_𝑎=𝑢, 𝑏_𝑏=𝑚

## Slide 181: Two-bit PM Critical Path
GCD update:
Add odd constant when divisibility of does not match that of
XGCD update:
Notes: May not be clear…
(details in paper)
Bring back time here?

## Slide 182: Euclid critical path
Compute
Compute
Most quotients in Euclid’s algorithm are small for 1024-bit inputs
Can estimate few of the most significant bits of for faster execution
Get MSBs
LUT
Compute
Notes: HW block diagram
LUT -> computes q * b -> stacked adders with partial products
Compute remainder goes into another adder

## Slide 183: Euclid critical path
Computing the remainder
Compute
Compute
Compute
Get MSBs
LUT
Multiplier
Notes: HW block diagram
LUT -> computes q * b -> stacked adders with partial products
Compute remainder goes into another adder

## Slide 184: Euclid critical path
Computing the remainder
Compute
Compute
Compute
Get MSBs
LUT
Multiplier
Notes: HW block diagram
LUT -> computes q * b -> stacked adders with partial products
Compute remainder goes into another adder

## Slide 185: Critical paths primarily require additions
The fastest adder is a carry-save adder (CSA)
  Eliminates carry propagation, requiring delay
  Stores numbers in CSA form or redundant binary form
1 1 1 0
1 1 0 1 (a)
1 1 1 0 (b)
0 0 1 0 (c)
----------------
1 1 1 0 1
1 1 0 1 (a)
1 1 1 0 (b)
0 0 1 0 (c)
-------------------
0 0 0 1 sum
1 1 1 0 0 carry
-------------------
1 1 1 0 1
Notes: Both critical paths require additions
  Two-bit PM adds
  Euclid requires multiplying , which adds partial products, and subtracts to get the remainder
Both critical paths require additions
  Two-bit PM adds 𝑢 + 𝑦 + 3𝐵
  Euclid requires multiplying 𝑞∗𝑏, which adds partial products, and subtracts 𝑎−𝑞∗𝑏 to get the remainder

## Slide 186: Two-bit PM with 3:2 CSAs: 3 CSA Delays
CSA
CSA
CSA
Notes: Shift is nontrivial

## Slide 187: Euclid with CSAs
Compute
Compute
Compute
Get MSBs
LUT
Require 6-bit normal adds to get MSBs of
CSA delays
Notes: HW block diagram
LUT -> computes q * b -> stacked adders with partial products
Compute remainder goes into another adder

## Slide 188: Euclid with CSAs: 9 CSA delays
Compute
Compute
Compute
Computing the remainder
Get MSBs
LUT
Multiplier
Add 14 values with CSAs CSA delays
Require 6-bit normal adds to get MSBs of
CSA delays
Notes: HW block diagram
LUT -> computes q * b -> stacked adders with partial products
Compute remainder goes into another adder

## Slide 189: Two-bit PM is a faster starting point
Two-bit PM critical path delay estimate is 3X shorter than Euclid’s
Two-bit PM iteration counts are at most 2X higher than Euclid’s
Two-bit PM with carry-save adders is the more promising starting point for hardware in the average and the worst-case.

## Slide 190: Our unified design with constant-time config
[DdPM+21]
[BY19]
[Por20]
Our work
Approach
Termination Condition
Pad to worst-case cycle count
Cycle count equal to worst case
Reduce inputs until GCD
or
vs
CT
NCT
Application Requirements
Note that since are in CSA form, we do not know when they become
Notes: Constant-power?

## Slide 191: We focus on the optimal design space
Software
NCT
CT
NCT
CT
Hardware
NCT
CT
Target Platform
Algorithm
Application Requirements
[AHAJS16]
[ZST+20]
[ZTW21]
[DdPM+21]
[BY19]
[Por20]
CT = constant-time, NCT = not constant-time
Unified
Our work

## Slide 192: Is three-bit PM faster in hardware?
Chart: Clock Frequency (GHz)
| 5.1813471502590671 | 4.5871559633027523 | 3.9840637450199203 | 4.2735042735042734 | 4.048582995951417 | 3.8910505836575875 | 3.3670033670033672 | 3.125 | 3.0303030303030303
 | 2210 | 1845 | 1740 | 1450 | 1211 | 1143 | 1091 | 972 | 937
Yes, three-bit PM has lowest average execution time
Data labels: (reduction factor even, reduction factor odd): Average execution time
Notes: Maybe cut?
Refer to paper
Tradeoff between cycle count and freq

## Slide 193: Is three-bit PM faster in hardware?
Chart: Clock Frequency (GHz)
| 5.1813471502590671 | 4.5871559633027523 | 3.9840637450199203 | 4.2735042735042734 | 4.048582995951417 | 3.8910505836575875 | 3.3670033670033672 | 3.125 | 3.0303030303030303
 | 2210 | 1845 | 1740 | 1450 | 1211 | 1143 | 1091 | 972 | 937
Data labels: (reduction factor even, reduction factor odd): Average execution time
No, all have same worst-case cycle count
Max frequency
Notes: Maybe cut?

## Slide 194
Notes: Other tricks to make clock frequency higher

## Slide 195
Functionality: Preserve sign and correct truncated results when shifting in CSA form

## Slide 196
Termination condition samples every four cycles
Pre- and post-processing run at ¼ main clock frequency for non-CSA adds
Notes: Confusing…
HW is used much -> turn it off for most of time
Check if at 0
Need carry propagation
Still 0
Subsample a, b to check for 0

## Slide 197
Minimize control overhead with larger reduction factors
Compute update options in parallel and use late selects
Precompute control signals

## Slide 198: Critical Path in 16nm
1024 bits
255 bits
Notes: Sums are the same up until clock skew
Clock skew definition
- Different bitwidths: critical paths are same
however, build a chip -> smaller 255 -> longer wires -> clock skew
Physical design -> contributor to difference
Ideal versions of circuits = same clock speed
Physical limitation

## Slide 199: 255-bit Constant-time XGCD Comparison
Notes: Lines are constant execution time
Iso-performance lines
Bottom right is better
Clean up graph
FPGA speed up
Our design is in an previously unexplored part of the design space
, first constant-time ASIC

## Slide 200: 1024-bit XGCD Comparison

## Slide 201: Our design impacts application approaches
Supports progression in state of the art for Curve25519
  To point multiplication algorithms that use more inversions
Informs reasonable security levels for this type of VDF
  Since our hardware is 30 to 40X faster than software
Other suggestions?
Notes: Exponentiation mod p
Fixed exp, variable base
Check if in multiplicative subgroup
Fastest possible multiplication algorithm for fixed exponent
Addition chains (current state of the art)
1.5 * n -> ops
Addition-subtraction chain (generalization) -> sum/diff between two prior values in chain
Divisions instead of multiplications for exponentiation mod p

## Slide 202: Our design impacts application approaches
Supports progression in state of the art for Curve25519
  To point multiplication algorithms that use more inversions
Informs reasonable security levels for this type of VDF
  Since our hardware is 30 to 40X faster than software
Our work is open-source!
https://github.com/kavyasreedhar/sreedhar-xgcd-hardware-ches2022

## Slide 203: DRAFT

## Slide 204: Our design impacts application approaches
Supports progression in state of the art for Curve25519
  To using constant-time XGCD for inversion
Notes: Exponentiation mod p
Fixed exp, variable base
Check if in multiplicative subgroup
Fastest possible multiplication algorithm for fixed exponent
Addition chains (current state of the art)
1.5 * n -> ops
Addition-subtraction chain (generalization) -> sum/diff between two prior values in chain
Divisions instead of multiplications for exponentiation mod p

## Slide 205: Our design impacts application approaches
Supports progression in state of the art for Curve25519
  To using constant-time XGCD for inversion
Informs reasonable security levels for this type of VDF
  Since our XGCD hardware is 36X faster than software
Notes: Exponentiation mod p
Fixed exp, variable base
Check if in multiplicative subgroup
Fastest possible multiplication algorithm for fixed exponent
Addition chains (current state of the art)
1.5 * n -> ops
Addition-subtraction chain (generalization) -> sum/diff between two prior values in chain
Divisions instead of multiplications for exponentiation mod p

## Slide 206: Our design impacts application approaches
Supports progression in state of the art for Curve25519
  To using constant-time XGCD for inversion
Informs reasonable security levels for this type of VDF
  Since our XGCD hardware is 36X faster than software
May be useful for other applications?
Notes: Exponentiation mod p
Fixed exp, variable base
Check if in multiplicative subgroup
Fastest possible multiplication algorithm for fixed exponent
Addition chains (current state of the art)
1.5 * n -> ops
Addition-subtraction chain (generalization) -> sum/diff between two prior values in chain
Divisions instead of multiplications for exponentiation mod p

## Slide 207: Our design impacts application approaches
Supports progression in state of the art for Curve25519
  To using constant-time XGCD for inversion
Informs reasonable security levels for this type of VDF
  Since our XGCD hardware is 36X faster than software
May be useful for other applications?
https://github.com/kavyasreedhar/sreedhar-xgcd-hardware-ches2022
Notes: Exponentiation mod p
Fixed exp, variable base
Check if in multiplicative subgroup
Fastest possible multiplication algorithm for fixed exponent
Addition chains (current state of the art)
1.5 * n -> ops
Addition-subtraction chain (generalization) -> sum/diff between two prior values in chain
Divisions instead of multiplications for exponentiation mod p

## Slide 208: Two-bit PM critical path: 3 CSA delays
CSA
CSA
CSA
Notes: Shift is nontrivial

## Slide 209: 255-bit Constant-time XGCD Comparison
Chart: 
| 2.2999999999999998 | 2.2999999999999998 | 0.20699999999999999 | 0.44700000000000001 | 4.55
Cycles | 8543 | 6253 | 8466 | 386 | 386
Clock Frequency (GHz)
100
105
103
104
102
101
Cycle Count
[BY19]: 3.7
[Por20]: 2.7
[DdPM+21]: 41
Better
Ours: 0.085
Ours: 0.863
* Times are in us
Direct FPGA Comparison
Our design is 48X faster
Software
FPGA
ASIC

## Slide 210
Clock Frequency (GHz)
1024-bit XGCD Comparisons
100
105
103
104
102
101
Cycle Count
Better
Software
FPGA
ASIC
Our ASIC
36X faster than software
8X faster than state-of-the-art ASIC
Direct FPGA Comparison
Our design is 3X faster
Chart: 
| 3.9940000000000003E-2 | 0.248 | 0.25 | 0.5 | 3.89 | 1
Cycles | 598 | 1143 | 1623 | 3000 | 1143 | 10650
[ZTW21]: 6.5
[AHAJS16]: 15
[ZST+20]: 6
Ours: 4.6
Ours: 0.294
* Times are in us
GNU C++ on Apple M1: 10.7

## Slide 211
Chart: 
| 2.2999999999999998 | 2.2999999999999998 | 0.20699999999999999 | 0.44700000000000001 | 4.55
Cycles | 8543 | 6253 | 8466 | 386 | 386
Clock Frequency (GHz)
255-bit Constant-time XGCD Comparisons
100
105
103
104
102
101
Cycle Count
[BY19]: 3.7
[Por20]: 2.7
[DdPM+21]: 41
Better
Software
FPGA
ASIC
Ours: 0.085
Ours: 0.863
Our ASIC
32X faster than [Por20]
First for constant-time 255-bit XGCD
Direct FPGA Comparison
Our design is 48X faster
* Times are in us

## Slide 212: Critical Path in 16nm
 | 1024-bit XGCD | 255-bit XGCD
DFF clk to Q | 45 | 40
Inverter | 7 | 0
CSA | 18 | 39
CSA | 31 | 39
Buffer | 13 | 0
CSA | 30 | 34
Shift in CSA form | 15 | 18
Late select muxes | 18 | 18
Precomputing control | 27 | 22
Setup Time | 2 | 5
Total | 206 | 215
Notes: Sums are the same up until clock skew
Clock skew definition
- Different bitwidths: critical paths are same
however, build a chip -> smaller 255 -> longer wires -> clock skew
Physical design -> contributor to difference
Ideal versions of circuits = same clock speed
Physical limitation
Critical path is what we expected
Different bitwidths
Clock skew

## Slide 213: Is three-bit PM faster in hardware?
Chart: Clock Frequency (GHz)
| 5.1813471502590671 | 4.5871559633027523 | 3.9840637450199203 | 4.2735042735042734 | 4.048582995951417 | 3.8910505836575875 | 3.3670033670033672 | 3.125 | 3.0303030303030303
 | 2210 | 1845 | 1740 | 1450 | 1211 | 1143 | 1091 | 972 | 937
Yes, three-bit PM has lowest average execution time
Data labels: (reduction factor even, reduction factor odd): Average execution time
Notes: Maybe cut?
Refer to paper
Tradeoff between cycle count and freq

## Slide 214: Is three-bit PM faster in hardware?
Chart: Clock Frequency (GHz)
| 5.1813471502590671 | 4.5871559633027523 | 3.9840637450199203 | 4.2735042735042734 | 4.048582995951417 | 3.8910505836575875 | 3.3670033670033672 | 3.125 | 3.0303030303030303
 | 2210 | 1845 | 1740 | 1450 | 1211 | 1143 | 1091 | 972 | 937
Data labels: (reduction factor even, reduction factor odd): Average execution time
No, all have same worst-case cycle count
Max frequency
Notes: Maybe cut?

## Slide 215: GCD Algorithms Comparison
Algorithm
[BY19]
[Por20]
Iterative Operation
GCD-preserving Transformation
Subtraction (Base: Stein)
Division (Base: Euclid)
vs
Notes: Shifts when are even
Two-bit PM algorithm reduces a factor
Shifts when 𝑎,𝑏 are even
Two-bit PM algorithm reduces a factor

## Slide 216: GCD Algorithms Comparison
Algorithm
[DdPM+21]
[BY19]
[Por20]
Our work
Iterative Operation
GCD-preserving Transformation
Worst-Case Iterations
Subtraction (Base: Stein)
387 *
Division (Base: Euclid)
384
vs
for 255-bit inputs
1X
* [YZ86]
Notes: list average and worst-case iterations for both
Subtraction is faster for constant-time XGCD
We observed all hardware papers built from efficient algorithms chosen in efficient software implementations. We look at if this is optimal.
Iteration time = Longest series of data-dependent operations
Since software is constrained to using instructions predefined in the processor’s instruction set architecture (ISA), software iteration times correspond to the longest set of dependent instructions. In contrast, hardware is not limited to an ISA and allows for implementing fast, wide, and custom datapaths with extremely short iteration times.

## Slide 217: GCD Algorithms Comparison
Algorithm
[DdPM+21]
[BY19]
[Por20]
Our work
Iterative Operation
GCD-preserving Transformation
Worst-Case Iterations
Average Iterations
Subtraction (Base: Stein)
387 *
1195 *
Division (Base: Euclid)
384
598
vs
for 255-bit inputs
1X
for 1024-bit inputs
2X
* [YZ86]
Notes: A 2X difference is not large, why not in software?
Intuition is division is faster, software do not seem to do two-bit PM
Could be faster in software
Multiple subtractions
Two-bit in software
Is subtraction twice as fast as divison?
We extend the two-bit PM algorithm for extended GCD
We observed all hardware papers built from efficient algorithms chosen in efficient software implementations. We look at if this is optimal.
Iteration time = Longest series of data-dependent operations
Since software is constrained to using instructions predefined in the processor’s instruction set architecture (ISA), software iteration times correspond to the longest set of dependent instructions. In contrast, hardware is not limited to an ISA and allows for implementing fast, wide, and custom datapaths with extremely short iteration times.

## Slide 218: State of the world post our work
This approach gives order-of-magnitude better performance
  30 – 40X faster than software
  8X faster than state-of-the-art ASIC and first constant-time ASIC
In a 16nm technology, our hardware design runs at 4+ GHz clock frequencies and leverages further optimizations to achieve state-of-the-art performance for both average- and worst-case XGCD execution. It is 8× faster than the state-of-the-art ASIC for 1024-bit XGCD and 32× faster than the state-of-the-art software for constant-time 255-bit XGCD,
1) order of magnitude faster XGCD
2) motivating applications
  Competitive (and the only) ASIC point for NUDUPL
  Elliptic curves -> progression in the state of the art from FLT to XGCD

## Slide 219: XGCD algorithms iteratively transform inputs
Algorithm
[BY19]
[Por20]
Iterative Operation
GCD-preserving Transformation
Subtraction (Base: Stein)
Division (Base: Euclid)
vs
Notes: Shifts when are even
Can reduce by factors of 2
Shifts when 𝑎,𝑏 are even
Can reduce by factors of 2

## Slide 220: Subtraction is faster for constant-time XGCD
Algorithm
[DdPM+21]
[BY19]
[Por20]
Our work
Iterative Operation
GCD-preserving Transformation
Worst-Case Iterations
Subtraction (Base: Stein)
387 *
Division (Base: Euclid)
384
vs
for 255-bit inputs
1X
* [YZ86]
Notes: We observed all hardware papers built from efficient algorithms chosen in efficient software implementations. We look at if this is optimal.
Iteration time = Longest series of data-dependent operations
Since software is constrained to using instructions predefined in the processor’s instruction set architecture (ISA), software iteration times correspond to the longest set of dependent instructions. In contrast, hardware is not limited to an ISA and allows for implementing fast, wide, and custom datapaths with extremely short iteration times.

## Slide 221: Is subtraction twice as fast as division?
Algorithm
[DdPM+21]
[BY19]
[Por20]
Our work
Iterative Operation
GCD-preserving Transformation
Worst-Case Iterations
Average Iterations
Subtraction (Base: Stein)
387 *
1195 *
Division (Base: Euclid)
384
598
vs
for 255-bit inputs
1X
for 1024-bit inputs
2X
* [YZ86]
Notes: We observed all hardware papers built from efficient algorithms chosen in efficient software implementations. We look at if this is optimal.
Iteration time = Longest series of data-dependent operations
Since software is constrained to using instructions predefined in the processor’s instruction set architecture (ISA), software iteration times correspond to the longest set of dependent instructions. In contrast, hardware is not limited to an ISA and allows for implementing fast, wide, and custom datapaths with extremely short iteration times.

## Slide 222: Hardware allows for short iteration times
Algorithm
[DdPM+21]
[BY19]
[Por20]
Our work
Iterative Operation
GCD-preserving Transformation
Average Iterations
Worst-Case Iterations
Subtraction (Base: Stein)
1195 *
387 *
Division (Base: Euclid)
598
384
vs
for 1024-bit inputs
2X
for 255-bit inputs
1X
Notes: We observed all hardware papers built from efficient algorithms chosen in efficient software implementations. We look at if this is optimal.
Iteration time = Longest series of data-dependent operations
Since software is constrained to using instructions predefined in the processor’s instruction set architecture (ISA), software iteration times correspond to the longest set of dependent instructions. In contrast, hardware is not limited to an ISA and allows for implementing fast, wide, and custom datapaths with extremely short iteration times.

## Slide 223: Hardware allows for short iteration times
Algorithm
[DdPM+21]
[BY19]
[Por20]
Our work
Iterative Operation
Base Algorithm
GCD-preserving transformation
Subtraction
Stein
Division
Euclid
vs
Notes: We observed all hardware papers built from efficient algorithms chosen in efficient software implementations. We look at if this is optimal.
Iteration time = Longest series of data-dependent operations
Since software is constrained to using instructions predefined in the processor’s instruction set architecture (ISA), software iteration times correspond to the longest set of dependent instructions. In contrast, hardware is not limited to an ISA and allows for implementing fast, wide, and custom datapaths with extremely short iteration times.

## Slide 224: Algorithms use GCD-preserving transformations
Stein
Euclid

## Slide 225: Current view of XGCD design space is narrow
Software
Hardware
Stein
NCT
CT
Euclid
NCT
CT
Stein
NCT
CT
Euclid
NCT
CT

## Slide 226: Current view of XGCD design space is narrow
Software
Hardware
Stein
Euclid
Stein
Euclid
Non-CT
CT
Stein
Non-CT
CT

## Slide 227: There is an increasing need for faster XGCD
Curve25519 Modular Inversion
Squaring binary quadratic functions (VDF eval)
Extended GCD (XGCD)
Constant-time
Non-constant-time
255-bit inputs
100% of execution time
Inputs: 833 [HM00] to 3000+ [DGS20] bits 91% of execution time
2021
2021
[BY19] : constant-time XGCD can be faster than Fermat’s Little Theorem
833 bits [HM00] to 3000+ bits [DGS20]
[Ber 06]
Notes: Fermat Little Theorem background
Modular inversion first

## Slide 228: Extended GCD is widely used in cryptography
Modular Multiplicative Inverse
RSA
Elliptic Curve Cryptography
ElGamal Encryption
.
.
.

## Slide 229: There is an increasing need for faster XGCD
Extended GCD (XGCD)
Non-constant-time
Constant-time
Extended GCD (XGCD) computes satisfying Bézout Identity

## Slide 230: There is an increasing need for faster XGCD
Verifiable Delay Functions (VDFs)
Extended GCD (XGCD)
Non-constant-time
1024-bit XGCD
91% of execution time
2018 [1]
[1] Boneh et al. Verifiable delay functions. Crypto 2018.
[2] Bernstein and Yang. Fast constant-time gcd computation and modular inversion. CHES 2019.
Constant-time

## Slide 231: There is an increasing need for faster XGCD
Verifiable Delay Functions (VDFs)
Modular Inversion for Elliptic Curve25519
Extended GCD (XGCD)
Non-constant-time
Constant-time
1024-bit XGCD
91% of execution time
255-bit XGCD
100% of execution time
2018 [1]
2021 [2]
[1] Boneh et al. Verifiable delay functions. Crypto 2018.
[2] Bernstein and Yang. Fast constant-time gcd computation and modular inversion. CHES 2019.
Notes: Fermat Little Theorem background
Modular inversion first

## Slide 232: How fast can one do XGCD?
Chart: 1024-bit XGCD
| 3.9940000000000003E-2 | 0.248 | 0.25 | 0.5 | 3.89
Cycles | 598 | 1143 | 1623 | 3000 | 1143
Chart: 255-bit constant-time XGCD
| 2.2999999999999998 | 2.2999999999999998 | 0.20699999999999999 | 0.44700000000000001 | 4.55
Cycles | 8543 | 6253 | 8466 | 386 | 386
Legend
Software
FPGA
ASIC
No ASIC points!
Notes: Symbols, stars/circles/squares/triangles

## Slide 233: Current view of XGCD design space is narrow
Few papers explore XGCD hardware
Moreover, these papers offer point solutions
All prior hardware papers build from Euclid’s algorithm
We explore the broader design space to understand
Can we significantly improve XGCD performance with hardware?

## Slide 234: We explore the broader design space
Few existing papers offer point solutions
All prior hardware papers build from Euclid’s algorithm
Notes: Design space: algorithm, platform (hardware splits into FPGA, ASIC), application requirements
cites

## Slide 235: Hardware vs software framing
Hardware implementations were following optimal software point
We reconsider the space for hardware
Intuition

## Slide 236: XGCD accelerator design space
Optimal algorithmic choice for hardware
Large-integer arithmetic circuit optimizations
Different application requirements
Notes: Low iteration count
Most software implementations also use Euclid’s algorithm, so hardware has followed suited
However, software is limited by the underlying processor’s ISA while hardware is not
In hardware, we can explicitly define the operations that occur in a clock cycle and design hardware for aggressively short cycle times
We found that this additional control over cycle time opens the opportunity to acceleration subtraction-based algorithms that require more iterations but far simpler operations
Low iteration count
All prior hardware works accelerate Euclid’s algorithm
Key Insight – We make the key observation that the additional influence that hardware 261 has on iteration time opens the opportunity to select different XGCD algorithms that 262 require a greater number of iterations but have far simpler operations that hardware 263 exploits to significantly reduce iteration time, resulting in faster overall execution times.

## Slide 237: Algorithm branching

## Slide 238: Critical Paths

## Slide 239: CSAs
**hardware-only optimization
Does not translate to software

## Slide 240: Cycles

## Slide 241: XGCD accelerator design space
Optimal algorithmic choice for hardware
Large-integer arithmetic circuit optimizations
Different application requirements
Prior hardware work:
Directly adds large integers or suggests using carry-save adders
Our ASIC design:
Uses carry-save adders and addresses related challenges

## Slide 242: XGCD accelerator design space
Optimal algorithmic choice for hardware
Large-integer arithmetic circuit optimizations
Different application requirements
Prior hardware work:
Builds from
division-based algorithms
Our ASIC design:
Builds from subtraction-based algorithms
Notes: Low iteration count
Most software implementations also use Euclid’s algorithm, so hardware has followed suited
However, software is limited by the underlying processor’s ISA while hardware is not
In hardware, we can explicitly define the operations that occur in a clock cycle and design hardware for aggressively short cycle times
We found that this additional control over cycle time opens the opportunity to acceleration subtraction-based algorithms that require more iterations but far simpler operations
Low iteration count
All prior hardware works accelerate Euclid’s algorithm
Key Insight – We make the key observation that the additional influence that hardware 261 has on iteration time opens the opportunity to select different XGCD algorithms that 262 require a greater number of iterations but have far simpler operations that hardware 263 exploits to significantly reduce iteration time, resulting in faster overall execution times.

## Slide 243: Constant-time
Carry-save adders

## Slide 244: XGCD accelerator design space
Optimal algorithmic choice for hardware
Large-integer arithmetic circuit optimizations
Different application requirements
Prior hardware work:
provides point solutions targeting an application space
Our ASIC design:
Can evaluate fast average and constant-time XGCD
Notes: Low iteration count
All prior hardware works accelerate Euclid’s algorithm
Key Insight – We make the key observation that the additional influence that hardware 261 has on iteration time opens the opportunity to select different XGCD algorithms that 262 require a greater number of iterations but have far simpler operations that hardware 263 exploits to significantly reduce iteration time, resulting in faster overall execution times.

## Slide 245: We extend two-bit PM for XGCD

## Slide 246: Is three-bit PM faster in hardware?
Yes, three-bit PM has lowest average execution time
1024 bits
Notes: Pictures – cycles vs time
5% of cycles

## Slide 247: Is three-bit PM faster in hardware?
No, all these cases have same worst-case execution time.
1024 bits
For constant-time
Notes: Worst-case – they’re all the same

## Slide 250
Pre- and post-processing run at main clock frequency for carry-propagate adds

## Slide 251
Termination condition samples every four cycles

## Slide 252
Preserve sign and correct truncated results when shifting in CSA form

## Slide 253
Minimize control overhead
Compute update options in parallel and use late selects
Precompute control signals

## Slide 254: Results

## Slide 255: Critical Path in 16nm
1024 bits
255 bits
Notes: Local clock gating – turn balancing back on in flow
Couple levels of muxing
Precompute control for next cycle -> has to control everything (high fanout) -> high buffer delay affecting critical path

## Slide 256: Our work is open source!
https://github.com/kavyasreedhar/sreedhar-xgcd-hardware-ches2022
  Functional Model
  Hardware Generator
  Physical Design Scripts
    SKY 130nm – Full Flow
    TSMC 16nm – Synthesis

## Slide 257: State of the world post our work
1) order of magnitude faster XGCD
2) motivating applications
  Competitive (and the only) ASIC point for NUDUPL
  Elliptic curves -> progression in the state of the art from FLT to XGCD

## Slide 258: How fast can one do XGCD?
Chart: 255-bit constant-time XGCD
| 2.2999999999999998 | 2.2999999999999998
Software | 8543 | 6253
FPGA | 8466
Better
Notes: Legend
No ASIC points, state of the art is 2X faster
- Bold arrow that says better for lower right
Prototypes on FPGAs, we also did a prototype on FPGA and showed improvement
Axis, lines = execution time, faster slower
Not that many papers
ASIC – no ASIC 255-bit, 2x faster in 1024-bit
Not only are there not that many papers, transition

## Slide 259: How fast can one do XGCD?
Chart: 255-bit constant-time XGCD
| 2.2999999999999998 | 2.2999999999999998
Software | 8543 | 6253
FPGA | 8466
Chart: 1024-bit XGCD
| 3.9940000000000003E-2
FPGA | 598
ASIC | 1623 | 3000
GNU C++ on Apple M1
Better
Better
Notes: Legend
No ASIC points, state of the art is 2X faster
- Bold arrow that says better for lower right
Prototypes on FPGAs, we also did a prototype on FPGA and showed improvement
Axis, lines = execution time, faster slower
Not that many papers
ASIC – no ASIC 255-bit, 2x faster in 1024-bit
Not only are there not that many papers, transition

## Slide 260
Chart: 
| 2.2999999999999998 | 2.2999999999999998 | 0.20699999999999999 | 0.44700000000000001 | 4.55
Cycles | 8543 | 6253 | 8466 | 386 | 386
Chart: 
| 3.9940000000000003E-2 | 0.248 | 0.25 | 0.5 | 3.89 | 1
Cycles | 598 | 1143 | 1623 | 3000 | 1143 | 10650
Clock Frequency (GHz)
Clock Frequency (GHz)
1024-bit XGCD
255-bit constant-time XGCD
100
105
103
104
102
101
Cycle Count
[BY19]
[Por20]
[DdPM+21]
[ZTW21]
[AHAJS16]
[ZST+20]
Better
Better
No ASIC points
[ZST+20] is 2X faster than C++
Software
FPGA
ASIC
Legend
Notes: Legend
No ASIC points, state of the art is 2X faster
- Bold arrow that says better for lower right
Prototypes on FPGAs, we also did a prototype on FPGA and showed improvement
Axis, lines = execution time, faster slower
Not that many papers
ASIC – no ASIC 255-bit, 2x faster in 1024-bit
Not only are there not that many papers, transition